Battery Charging

Meets ASE Task:  (A6-B-5)  Perform battery charge.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Measure the open-circuit voltage of the battery =  ______ volts (red lead of the

voltmeter to positive [+] and black lead to negative [-]).  (If more than 12.6 V, remove

the surface charge by turning on the headlights for 1 minute).

_____  2.  Percentage of charge = ______%.

12.6 V or higher = 100% charged

12.4 V                =  75% charged

12.2 V                =  50% charged

12.0 V                =  25% charged

below 11.9 V     =  discharged

_____  3.  Determine the cold cranking amperes

(CCA) of the battery = __________.

(The charge rate should be 1% of the CCA.  For example, a battery with a 500 CCA rating should be charged at 5 ampere rate.)  Charge Rate = CCA

100

_____  4.  Determine the reserve capacity in minutes = _________.

(The charge rate can be determined by dividing the reserve capacity of the battery in minutes by 30.  For example, a 180-minute battery should be charged at 6 ampere rate: 180/30 = 6).

Charge Rate = Reserve Capacity

30

_____  5.  The battery should be charged at _____ amperes

(CCA method) or at _____ amperes (reserve

capacity method).