Starter Current Draw Test

Meets ASE Task:  (A6-C-1 and A6-C-6)  Perform starter current draw tests; determine needed action.  Differentiate between electrical and engine mechanical problems. (P-1 & P-2)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified starter current draw test procedure and

specifications and differentiate between electrical and engine mechanical problems.

__________________________________________________________________

__________________________________________________________________

NOTE:  Few vehicle manufacturers give starter current draw specifications with the starter installed on the vehicle.  Use the chart below as a guideline regarding the range of the maximum allowable starter draw.

4-cylinder engines = 150 to 185 amperes maximum

6-cylinder engines = 160 to 200 amperes maximum

8-cylinder engines = 185 to 250 amperes maximum

_____  2.  Perform the starter current draw test

following the manufacturer’s

instructions.

Results:  ________ amperes

_____  3.  Based on the specifications and the test

results, what is the needed action?

___________________________

___________________________

___________________________

___________________________

___________________________