Charging System Output Test

Meets ASE Task:  (A6-D-1)  Perform charging system output test; determine needed action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified charging system output test procedures

and specifications.

__________________________________________________________________

_____  2.  Connect the starting and charging test unit (such as a Sun VAT-40) leads to the battery

as per the manufacturer's instructions.

_____  3.  Attach the amp probe around the alternator output wire.

_____  4.  Start the engine and operate at 2,000 RPM (fast idle).

_____  5.  Turn the "load increase" control slowly to obtain the highest reading on the ammeter

scale.  (Do not let the battery voltage drop to less than 12 volts.)

Tested amps = __________ amps.

_____  6.  Specification (should be stamped on the alternator) or indicated by a

colored tag on or near the output terminal)  = _________ amps.

_____  7.  Results should be within 10% of the specifications.  If the alternator amperage output

is low, first check the condition of the alternator drive belt.  The alternator should not

be able to be rotated by hand with the engine "off."

OK_____   NOT OK_____

_____  8.  Based on the results of the charging system

output test, what is the needed action?

__________________________________________________________________

__________________________________________________________________