Alternator Stator Testing

Meets ASE Task:  Not specified by ASE

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Identify the type of stator.

_____ Wye (has three terminals with one wire at

each terminal and a wire junction)

_____ Delta (has three terminals with two wires

at each terminal)

_____  2.  Visually inspect the rotor for faults such as burned insulation due to overheating or

broken wires.

OK _____	NOT OK _____

_____  3.  Set a digital multimeter to read ohms (low

scale).

_____  4.  Measure the resistance between all three

terminals of the stator two at a time.  The

resistance will be low (usually less than 2 ohms).

If high or infinity, the stator is defective.

OK _____	NOT OK _____

_____  5.  To check if the stator windings are shorted-to-ground, connect one lead of the meter

(still set to read ohms) to the steel laminations of the stator and touch the other lead to

each of the three terminals.  The reading on all three terminals should be infinity (OL).

OK _____	NOT OK _____