Alternator Diode Trio Testing

Meets ASE Task:  Not specified by ASE

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Identify the type of alternator being serviced:

__________________________________

_____  2.  Visually check the diode trio for physical damage.

OK _____	NOT OK _____

_____  3.  Set a digital multimeter (DMM) to the diode-check position.

_____  4.  Touch the black lead of the meter to the output (single leg) of the diode trio.

_____  5.  Touch the red meter lead to each of the separate legs of the diode trio and record the

readings [should be 0.4 volt (400 mV) to 0.6 volt (600 mV)].

#1 = ____________

#2 = ____________

#3 = ____________

OK _____	NOT OK _____

_____  6.  Remove the meter leads and retest (should read OL).

#1 = ____________

#2 = ____________

#3 = ____________

OK _____	NOT OK _____