Alternator Rectifier Bridge Testing

Meets ASE Task:  Not specified by ASE

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Identify the type of  alternator.

_____ GM

_____ Ford

_____ Chrysler

_____ other (specify) _______________________________

_____  2.  How many diodes are used in the rectifier bridge (2 per stator winding)?

_____ 6

_____ 8

_____ other (specify) ________________

_____  3.  Visually check the rectifier bridge for physical

damage.

OK _____	NOT OK _____

_____  4.  Set a digital multimeter to the diode check

position.

_____  5.  Touch one meter lead to the terminal of the diode and the other lead to the heat sink

for the same diode and record the reading.  Reverse the leads and record the second

reading.  A good diode should read infinity (OL) one way and record a voltage drop

reading of between 0.4 volt (400 mV) and 0.6 volt (600 mV) the other way.

reading for diode #1 = __________ and ___________

reading for diode #2 = __________ and ___________

reading for diode #3 = __________ and ___________

reading for diode #4 = __________ and ___________

reading for diode #5 = __________ and ___________

reading for diode #6 = __________ and ___________

OK _____	NOT OK _____