Cruise Control

Meets ASE Task:  (A6-G-1)  Diagnose incorrect operation of cruise control system; determine needed action.  (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for specified diagnostic test procedures.  ______________

_________________________________________________________________

_____  2.  Locate the cruise control schematic and determine the following information.

a.  Describe the location of the servo unit _______________________________

___________________________________________________________

b.  Describe the location of the transducer (controller) _____________________

___________________________________________________________

c.  Describe the location of the safety switches (electrical and/or vacuum) ______

____________________________________________________________

_____  3.  What fuse number (label) and amperage rating is used for the cruise control system?

a.  Fuse number (label) ________________________________

b.  Fuse rating _______________________________

_____  4.  Describe the location of the ground(s) for the

cruise control.  ______________________

_______________________________

_______________________________

_____  5.  Based on the diagnostic test results, what is

the needed action?  _________________

________________________________

________________________________

________________________________

__________________________________________________________________