MacPherson Strut Service

Meets ASE Task:  (A4-C-10)  Remove, inspect, and install strut cartridge or assembly, strut coil spring, insulators (silencers), and upper strut bearing mount.  (P-3)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the service information for the specified service procedure.

_______________________________________________________________

_______________________________________________________________

_______________________________________________________________

_____  2.  Safely support the vehicle on jacks and/or the

lift.

_____  3.  Remove the upper and lower attaching bolts

and nuts.

_____  4.  Carefully remove the MacPherson

strut assembly from the vehicle.

_____  5.  Compress the coil spring with the proper

equipment and replace the strut assembly.

Show the instructor the disassembled unit.

Instructor's OK _________

_____  6.  Reinstall the complete assembly.

NOTE:  The vehicle should be aligned after replacing the strut assembly.