### Steering Problem Diagnosis

Meets ASE Task:  (A4-A-2) Identify and interpret steering concerns; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  What is the stated customer concern? ______________________________________

_____  2.  Test drive the vehicle under the same condition and road surface types as stated by

the customer when the problem occurs and check the following.

Steers straight?			OK ____    NOT OK ____

Wanders?				OK ____    NOT OK ____

Noise during turns or corners?	OK ____    NOT OK ____

Hard steering when cold only?	OK ____    NOT OK ____

Hard steering when raining?		OK ____    NOT OK ____

Noise when steering?			OK ____    NOT OK ____

Looseness in steering wheel?		OK ____    NOT OK ____

Lack of steering control?		OK ____    NOT OK ____

Other concerns (describe) _________________________________________

________________________________________________________

_____  3.  When does the fault or concern occur?

___ During turns or cornering to the right

___ During turns or cornering to the left

___ During turns or cornering both to the right or the left

___ While driving straight ahead

___ Only when driving on a rough road

___ Only when turning into or out of a driveway

___ Other (describe) _____________________________________________

_____  4.  Based on the test drive, what components or systems could be the cause of the

suspension problem or concern?

________________________________________________________________

________________________________________________________________

_____  5.  What action will be needed to correct these concerns? ________________________

_________________________________________________________________

_________________________________________________________________