Steering and Suspension Concerns

Meets ASE Task:  (A4-E-1) Diagnose vehicle wander, drift, pull, hard steering, bump steer, memory steer, torque steer; determine necessary action.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check the service information to determine the alignment specifications.

Camber = __________    Caster = __________    Toe = ___________

_____  2.  Hoist the vehicle on the alignment rack and install the wheel sensors.

_____  3.  Compensate the wheel sensors.

_____  4.  Lower the vehicle and jounce (bounce) to center the suspension.

_____  5.  Read the rear camber and toe.

LR		  RR

Camber 	_____		 _____

Toe       	_____		 _____

Total rear toe =    _______

_____  6.  Read the front camber and toe.

LF		  RF

Camber 	_____		 _____

Toe       	_____		 _____

Total front toe =    _______

_____  7.  Perform a caster sweep to determine the front caster and SAI.

LF		  RF

Caster  	_____		 _____

SAI       	_____		 _____

Based on the alignment angles, what action is needed?  _____________________

__________________________________________________________________