## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 114
Tire Pressure Monitoring Systems
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
114.1 Explain why a tire-pressure monitoring system (TPMS) is used.
114.2 Discuss the TREAD Act.
114.3 Explain indirect and direct TPMS.
114.4 List the two types of TPMS pressure sensors.
114.5 Discuss TPMS sensor operation and the TPMS receiver.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
114.6 Explain direct TPMS diagnosis and TPMS diagnostic tools.
114.7 List replacement options for TPMS sensors.
114.8 Describe how to relearn TPMS sensors and the tools needed to service a TPMS.
114.9 This chapter will help prepare for ASE Suspension and Steering (A4) certification content area “E” (Wheel and Tire Diagnosis and Repair).

## Slide 4: NEED FOR TIRE PRESSURE MONITORING (1 OF 2)
Background
  A tire-pressure monitoring system (TPMS) is a system that detects a tire that has low inflation pressure and warns the driver.
There are two systems used:
  Indirect
  Direct
Low Tire Pressure Effects
  Reduced fuel economy, and tire life. Reduces handling and braking efficiency.

## Slide 5: NEED FOR TIRE PRESSURE MONITORING (2 OF 2)
Placard Cold Inflation Pressure
  The term placard cold inflation pressure is used in service information to indicate the specified tire inflation pressure.
  The “placard” is the driver’s side door jamb sticker that shows the tire size and the specified tire inflation pressure.
Temperature and Inflation Pressure
  The tires become warmer while the vehicle is being driven, so tires should be checked before the vehicle has been driven or allowed to cool after being driven.

## Slide 6: Figure 114.1 The tire-pressure placard (sticker) on the driver’s side door or door jamb indicates the specified tire pressure

## Slide 7: Chart 114-1 The effects of outside temperature on tire inflation, assuming a placard inflation pressure of 32 PSI. The tire inflation pressure changes 1 PSI for each 10 degrees change in temperature.

## Slide 8: Tech Tip

## Slide 9: Figure 114.2 Inflation pressure increases as the temperature increases. When checking or correcting inflation pressure when the tires are hot, add 2 to 4 PSI to the placard cold inflation pressure.

## Slide 10: QUESTION 1: ?
What are the two types of monitoring systems?

## Slide 11: ANSWER 1:
Direct and Indirect.

## Slide 12: TREAD ACT (1 OF 2)
The Transportation Recall Enhancement, Accountability, and Documentation (TREAD) Act requires that all vehicles be equipped with a tire-pressure monitoring system that will warn the driver in the event of an underinflated tire.
The National Highway Traffic Safety Administration (NHTSA) requires the installation of tire-pressure monitoring systems in passenger vehicles and light trucks manufactured after September 1, 2007 (2008 model year).

## Slide 13: TREAD ACT (2 OF 2)
Warning Lamp
  The FMVSS 138 specifies that the driver must be warned of a low tire inflation pressure by turning on an amber warning lamp.
Twenty-Five Percent Rule
  The TREAD Act specifies that the driver be warned if any tire inflation pressure drops by 25% or more from the placard cold inflation pressure.

## Slide 14: Chart 114-2 Placard inflation pressure compared with the pressure when the TPMS triggers a warning light.

## Slide 15: INDIRECT TPMS (1 OF 2)
Function
  The system uses speed sensors to detect differences in the speed of the wheels.
  An underinflated tire will rotate faster than a properly inflated tire.
Compensation for Cornering
  To compensate for this normal change in wheel rotation speed, the indirect tire-pressure monitoring system checks the diagonally opposed wheels.

## Slide 16: INDIRECT TPMS (2 OF 2)
Diagnosis of Indirect TPMS
  Verify the fault.
    Light on- low pressure
    Light flashing – system problem
  Check tire pressure
  Repair fault
Indirect TPMS Relearn Procedures
  Check service information for the exact steps to follow.
  Typically a reset and a test drive is involved.

## Slide 17: Figure 114.3 A tire with low inflation will have a shorter distance (radius) between the center of the wheel and the road and will therefore rotate faster than a tire that is properly inflated

## Slide 18: Figure 114.4 The speeds of the diagonally opposed wheels are added together and then compared to the other two wheels to check if one tire is rotating faster

## Slide 19: Figure 114.5 The indirect tire-pressure monitoring system has a reset switch that should be depressed after rotating or replacing tires

## Slide 20: DIRECT TPMS
Function
  Direct tire-pressure monitoring systems use individual pressure sensors located in each wheel to measure the inflation pressure.
Identifying the System
  Because of the variety of systems used, service information is needed to determine what type of system is on the vehicle before service work is started.

## Slide 21: TPMS PRESSURE SENSORS (1 OF 2)
Manufacturers
  The sensors are manufactured by a variety of manufacturers, including:
  Beru
  Lear
  Pacific
  Schrader
  Siemens
  TRW
Each sensor uses a 3-volt lithium ion battery that has a service life of 7 to 10 years.

## Slide 22: TPMS PRESSURE SENSORS (2 OF 2)
Types
  There are two basic types of pressure sensors used in direct pressure-sensing systems.
  Valve-stem-mounted sensor
  Banded sensors
Modes of Operation
  Active Mode
  Sleep Mode
  Alert Mode

## Slide 23: Figure 114.6 A clear plastic valve-stem tire-pressure monitoring sensor, showing the round battery on the right and the electronic sensor and transistor circuits on the left

## Slide 24: Figure 114.7 A conventional valve stem is on the right compared with a rubber TPMS sensor stem on the left. Notice the tapered and larger brass stem. The rubber TPMS sensor also uses a longer cap that makes it easy for a technician to spot that this is not a conventional rubber valve stem

## Slide 25: Figure 114.8 The parts of a typical clamp-in TPMS sensor. Notice the small hole used to monitor the inflation pressure. The use of stop leak can easily clog this small hole

## Slide 26: Figure 114.9 The three types of TPMS sensors most commonly found include the two stem-mounted rubber (snap-in) and aluminum (clamp-in), left and top, and the banded sensors (right)

## Slide 27: Animation: Tire Pressure Monitor System, TPMS (Normal) (The animation will automatically start in a few seconds)

## Slide 28: QUESTION 2: ?
What are the two types of direct sensors?

## Slide 29: ANSWER 2:
Stem mounted and band mounted.

## Slide 30: TPMS SENSOR OPERATION
Designs: The types of sensors include:
  Continuous-wave-type sensor
  Magnetically triggered-type sensor
  Pulse-width-modulated-type sensor
The two most commonly used frequencies are:
  315 MHz
  433.92 MHz (commonly listed as 434 MHz)

## Slide 31: TPMS RECEIVER
Locations
  The wireless TPMS receiver is housed in one of the following locations, depending on the vehicle:
  Remote keyless entry (RKE) receiver
  Body control module (BCM)
  Door module
  Individual antennas near each wheel well.

## Slide 32: Figure 114.10 Some vehicles display the actual measured tire pressure for each tire on a driver information display

## Slide 33: CASE STUDY

## Slide 34: Figure 114.11 The TPMS warning lamp on this vehicle is a separate light from the tire icon light that warns of low tire pressure. In this case, both warning lights were on all of the time

## Slide 35: Figure 114.12 The codes set were for low pressure and sensor signal failure

## Slide 36: Animation: Tire Pressure Monitor System, TPMS (With Tire Leak) (The animation will automatically start in a few seconds)

## Slide 37: TECH TIP

## Slide 38: Figure 114.13 A typical tire-pressure monitoring system tester. The unit should be held near the tire and opposite the valve stem if equipped with a wheel-mounted sensor, and near the valve stem if equipped with a valve-stem-type sensor

## Slide 39: TPMS DIAGNOSIS
Warning Lamp On (Not Flashing)
  Check the door placard for the specified tire inflation pressure.
  Check all tires using a known-accurate tire-pressure gauge.
  Inflate all tires to the specified pressure.
Warning Lamp Flashing
  TPMS sensor not properly registered with the system.
  Defective wheel sensors, such as a sensor with a dead battery.
  A fault in the receiver or module.

## Slide 40: Animation: Tire Pressure Monitor System, TPMS (Failed Sensor) (The animation will automatically start in a few seconds)

## Slide 41: Figure 114.14 A tire-pressure warning light can vary depending on the vehicle, but includes a tire symbol

## Slide 42: TPMS SENSOR ACTIVATIONS
Activation methods include:
  Using a magnet.
  Changing inflation pressure.
  Triggered by a handheld TPMS tester.

## Slide 43: Figure 114.15 A magnet is placed around the valve stem to reprogram some stem-mounted tire-pressure sensors

## Slide 44: QUESTION 3: ?
What are the three listed ways to actuate a TPMS sensor?

## Slide 45: ANSWER 3:
A magnet, changing tire pressure, and a handheld TPMS tester.

## Slide 46: TPMS DIAGNOSTIC TOOLS
TPMS diagnostic tools include a variety of scan tools and handheld testers.
Scan Tools
  Register sensors
  Perform initialization
  Monitor sensor values
Handheld Testers
  Sensor activation
  Sensor relearn
  Programming a new sensor

## Slide 47: Figure 114.16 When replacing a TPMS sensor, be sure to record the sensor ID because this needs to be entered into the system through the use of a tester or scan tool

## Slide 48: SENSOR REPLACEMENT OPTIONS
Original Equipment-Based Sensors
  These sensors are made by the original equipment (OE) manufacturer and usually are direct replacement for the factory unit.
Aftermarket Sensors
  Original equipment (OE)-based replacement.
  Multiple protocol sensors that can be programmed to match whatever the vehicle needs.
  Fully programmable sensor—also called clones. This type needs a separate programming device.

## Slide 49: TPMS SENSOR RELEARN
Most relearn procedures fall into one of four categories including:
  Auto relearn
  European Relearn
  Manual Relearn
  OBD Relearn

## Slide 50: Figure 114.17 The sensor relearn procedure is performed in the following order after the system has been placed in learn mode: LF, RF, RR, and then LR

## Slide 51: TPMS SENSOR SERVICE TOOLS
Whenever servicing a tire/wheel assembly that has a direct TPMS system, certain items are needed:
  Service Information
  Digital tire pressure gauge
  Tire valve core torque wrench
  Tire valve nut torque wrench
  Sensor service kit

## Slide 52: Figure 114.18 Always use an accurate, known-good tire-pressure gauge. Digital gauges are usually more accurate than mechanical gauges

## Slide 53: Figure 114.19 A clicker-type valve core tool ensures that the valve core is tightened to factory specifications

## Slide 54: Figure 114.20 An assortment of service parts that include all of the parts needed to service a stem-mounted TPMS sensor being installed after removal for a tire replacement or repair

## Slide 55: Video Links (Internet Access Required)
TPMS (time 1:20:05)
TPMS sensor replacement (time 2:50)
TPMS sensor replacement (time 1:21)

## Slide 56: Copyright