## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 124
Wheel Alignment Principles
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
124.1 Define wheel alignment and discuss alignment-related problems.
124.2 Define camber, caster, toe, and SAI.
124.3 Discuss included angle, scrub radius, turning radius, setback, thrust angle, and tracking.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
124.4 Explain the importance of four-wheel alignment.
124.5 This chapter will help prepare for ASE Suspension and Steering (A4) certification test content area “D” (Wheel Alignment Diagnosis, Adjustment, and Repair).

## Slide 4: DEFINITION OF WHEEL ALIGNMENT
A wheel alignment is the adjustment of the suspension and steering to ensure proper vehicle handling with minimum tire wear.
The change in alignment angles may result from one or more of the following conditions:
  Wear of the steering and the suspension components
  Bent or damaged steering and suspension parts
  Sagging springs, which can change the ride height of the vehicle and therefore the alignment angles

## Slide 5: ALIGNMENT RELATED PROBLEMS (1 OF 2)
Pull
  A pull is generally defined as a definite tug on the steering wheel toward the left or the right while driving straight on a level road.
Lead or Drift
  A lead or drift is a mild pull that does not cause a force on the steering wheel that the driver must counteract.
Road Crown Effects
  On a two-lane road, the center of the road is often higher than the berms, resulting in a road crown.

## Slide 6: ALIGNMENT RELATED PROBLEMS (2 OF 2)
Wander
  A wander is a condition where constant steering wheel corrections are necessary to maintain a straight-ahead direction on a straight, level road.
Stiff Steering or Slow Return to Center
  Hard to steer problems caused by tires, low fluid, or mechanical binding.
Tramp or Shimmy Vibrations
  Up and down or side-to-side vibrations caused by out of balance or defective tires and wheels.

## Slide 7: Figure 124.1 A pull is usually defined as a tug on the steering wheel toward one side or the other

## Slide 8: Figure 124.2 The crown of the road refers to the angle or slope of the roadway needed to drain water off the pavement

## Slide 9: Figure 124.3 Wander is an unstable condition requiring constant driver corrections

## Slide 10: CAMBER
Definition
  Camber is the inward or outward tilt of the wheels from true vertical as viewed from the front or rear of the vehicle.
  Camber can cause tire wear if not correct.
  Camber can cause pull if it is unequal side to side.
  Incorrect camber can cause excessive wear on wheel bearings.
  Camber is not adjustable on many vehicles.

## Slide 11: Figure 124.4 Positive camber. The dotted line represents true vertical, and the solid line represents the angle of the wheel

## Slide 12: Figure 124.5 Negative camber. The dotted line represents true vertical and the solid line represents the angle of the wheel

## Slide 13: Figure 124.6 Zero camber. Note that the angle of the tire is true vertical

## Slide 14: Figure 124.7 Excessive positive camber and how the front tires would wear due to the excessive camber

## Slide 15: Figure 124.8 Excessive negative camber and how the front tires would wear due to the excessive camber

## Slide 16: Figure 124.9 Positive camber tilts the tire and forms a cone shape that causes the wheel to roll away or pull outward toward the point of the cone

## Slide 17: Figure 124.10 Negative camber creates a pulling force toward the center of the vehicle

## Slide 18: Figure 124.11 If camber angles are different from one side to the other, the vehicle will pull toward the side with the most camber

## Slide 19: Figure 124.12 Positive camber applies the vehicle weight toward the larger inner wheel bearing. This is desirable because the larger inner bearing is designed to carry more vehicle weight than the smaller outer bearing

## Slide 20: Figure 124.13 Negative camber applies the vehicle weight to the smaller outer wheel bearing. Excessive negative camber, therefore, may contribute to outer wheel bearing failure

## Slide 21: Animation: Wheel Alignment: Camber (The animation will automatically start in a few seconds)

## Slide 22: QUESTION 1: ?
What is the effect of unequal camber?

## Slide 23: ANSWER 1:
  Camber can cause pull if it is unequal side to side.

## Slide 24: CASTER
Definition
  Caster is the forward or rearward tilt of the steering axis in reference to a vertical line as viewed from the side of the vehicle.
  Caster is not a tire-wearing angle, but positive caster does cause changes in camber during a turn.
  Caster is a stability angle.
  Caster can cause pull if unequal.
  Caster is not adjustable on many vehicles.
  Caster should be equal on both sides.

## Slide 25: Figure 124.14 Zero caster

## Slide 26: Figure 124.15 Positive (+) caster

## Slide 27: Figure 124.16 Negative (−) caster is seldom specified on today’s vehicles because it tends to make the vehicle unstable at highway speeds. Negative caster was specified on some older vehicles not equipped with power steering to help reduce the steering effort

## Slide 28: Figure 124.17 As the spindle rotates, it lifts the weight of the vehicle due to the angle of the steering axis

## Slide 29: Figure 124.18 Vehicle weight tends to lower the spindle, which returns the steering to the straight-ahead position

## Slide 30: Figure 124.19 High caster provides a road shock path to the vehicle

## Slide 31: Figure 124.20 A steering dampener is used on many pickup trucks, sport-utility vehicles (SUVs), and many luxury vehicles designed with a high-positive-caster setting. The dampener helps prevent steering wheel kickback when the front tires hit a bump or hole in the road.

## Slide 32: Figure 124.21 As the load increases in the rear of a vehicle, the top steering axis pivot point moves rearward, increasing positive (+) caster

## Slide 33: Tech Tip

## Slide 34: Figure 124.22 Note how the front tire becomes tilted as the vehicle turns a corner with positive caster. The higher the caster angle, the more the front tires tilt, causing camber-type tire wear

## Slide 35: Animation: Wheel Alignment: Caster (The animation will automatically start in a few seconds)

## Slide 36: QUESTION 2: ?
How does incorrect caster effect front tire wear?

## Slide 37: ANSWER 2:
  Caster is not a tire-wearing angle, but positive caster does cause changes in camber during a turn.

## Slide 38: TOE
Definition
  Toe is the difference in distance between the front and rear of the tires.
  Incorrect toe is the major cause of excessive tire wear!
  Incorrect front toe does not cause a pull condition.
  All vehicles can be adjusted for front toe.
  Many vehicle manufacturers specify a slight amount of toe-in to compensate for the natural tendency of the front wheels to spread apart (become toed-out).

## Slide 39: Figure 124.23 Zero toe. Note how both tires are parallel to each other as viewed from above the vehicle

## Slide 40: Figure 124.24 Total toe is often expressed as an angle. Because both front wheels are tied together through the tie rods and center link, the toe angle is always equally split between the two front wheels when the vehicle moves forward

## Slide 41: Figure 124.25 Toe-in, also called positive (+) toe

## Slide 42: Animation: Toe-in, RWD Vehicle (The animation will automatically start in a few seconds)

## Slide 43: Figure 124.26 Toe-out, also called negative (−) toe

## Slide 44: Animation: Toe-out, FWD Vehicle (The animation will automatically start in a few seconds)

## Slide 45: Figure 124.27 This tire is just one month old! It was new and installed on the front of a vehicle that had about 1/4 inch (6 mm) of toe-out. By the time the customer returned to the tire store for an alignment, the tire was completely bald on the inside.

## Slide 46: Figure 124.28 Excessive toe-out and the type of wear that can occur to the side of both front tires

## Slide 47: Figure 124.29 Excessive toe-in and the type of wear that can occur to the outside of both front tires

## Slide 48: Figure 124.30 Feather-edge wear pattern caused by excessive toe-in or toe-out

## Slide 49: Figure 124.31 Rear toe-in (+). The rear toe (unlike the front toe) can be different for each wheel while the vehicle is moving forward because the rear wheels are not tied together as they are in the front

## Slide 50: Figure 124.32 Incorrect toe can cause the tire to run sideways as it rolls, resulting in a diagonal wipe

## Slide 51: Figure 124.33 Diagonal wear such as shown here is usually caused by incorrect toe on the rear of a front-wheel-drive vehicle

## Slide 52: Figure 124.34 Toe on the front of most vehicles is adjusted by turning the tie rod sleeve, as shown

## Slide 53: TECH TIP

## Slide 54: Figure 124.35 While the feathered or sawtooth tire tread wear pattern may not be noticeable to the eye, this wear can usually be felt by rubbing your hand across the tread of the tire

## Slide 55: Animation: Wheel Alignment: Toe (The animation will automatically start in a few seconds)

## Slide 56: QUESTION 3: ?
What is the most significant effect of incorrect toe adjustment?

## Slide 57: ANSWER 3:
  Incorrect toe is the major cause of excessive tire wear!

## Slide 58: STEERING AXIS INCLINATION
The steering axis is the angle formed between true vertical and an imaginary line drawn between the upper and lower pivot points of the spindle.
The purpose of SAI is to provide an upper suspension pivot location that causes the spindle to travel in an arc when turning, which tends to raise the vehicle.

## Slide 59: Figure 124.36 The left illustration shows that the steering axis inclination angle is determined by drawing a line through the center of the upper and lower ball joints The right illustration shows that the steering axis inclination angle is determined by drawing a line through the axis of the upper strut bearing mount assembly and the lower ball joint

## Slide 60: Figure 124.37 The SAI causes the spindle to travel in an arc when the wheels are turned. The weight of the vehicle is therefore used to help straighten the front tires after a turn and to help give directional stability

## Slide 61: INCLUDED ANGLE
The included angle is the SAI added to the camber reading of the front wheels only.
Included angle is an important angle to measure for diagnosis of vehicle handling or tire wear problems.
For best handling both the included angle and SAI should be within 1/2 degree of the other side of the vehicle.

## Slide 62: Figure 124.38 Included angle on a MacPherson-strut-type suspension

## Slide 63: Animation: Wheel Alignment: Steering Axis Inclination & Included Angle (The animation will automatically start in a few seconds)

## Slide 64: Figure 124.39 Included angle on an SLA-type suspension. The included angle is the SAI angle and the camber angle added together

## Slide 65: Figure 124.40 Cradle placement. If the cradle is not replaced in the exact position after removal for a transmission or clutch replacement, the SAI, camber, and included angle will not be equal side to side

## Slide 66: SCRUB RADIUS
Scrub radius refers to the distance between the line through the steering axis and the centerline of the wheel at the contact point with the road surface.
Scrub radius is not adjustable and cannot be measured.
  A bent spindle can cause a change in the scrub radius.
  Changing tire or wheel sizes can affect scrub radius.

## Slide 67: Figure 124.41 A positive scrub radius (angle) is usually built into most SLA front suspensions, and a negative scrub radius is usually built into most MacPherson-strut type front suspensions

## Slide 68: Figure 124.42 With negative scrub radius, the imaginary line through the steering axis inclination (SAI) intersects the road outside of the centerline of the tire. With positive scrub radius, the SAI line intersects the road inside the centerline of the tires

## Slide 69: Figure 124.43 With a positive scrub radius, the pivot point, marked with a + mark, is inside the centerline of the tire and will cause the wheel to turn toward the outside, especially during braking. Negative scrub radius, as is used with most front-wheel-drive vehicles, generates an inward force on the tires

## Slide 70: TURNING RADIUS (TOE-OUT ON TURNS)
Whenever a vehicle turns a corner, the inside wheel has to turn at a sharper angle than the outside wheel because the inside wheel has a shorter distance to travel.
Turning radius is a nonadjustable angle.
Symptoms of out-of-specification turning angle include the following:
  Tire squeal noise during normal cornering.
  Scuffed tire wear

## Slide 71: Figure 124.44 To provide handling, the inside wheel has to turn at a greater turning radius than the outside wheel

## Slide 72: Animation: Wheel Alignment: Turning Radius (The animation will automatically start in a few seconds)

## Slide 73: Animation: Turning Radius (The animation will automatically start in a few seconds)

## Slide 74: Figure 124.45 The proper toe-out on turns is achieved by angling the steering arms

## Slide 75: SETBACK
Setback is the angle formed by a line drawn perpendicular (at 90 degrees) to the front axles.
Setback is a nonadjustable measurement, even though it may be corrected.
Setback can be measured with a four-wheel alignment machine.

## Slide 76: Figure 124.46 (a) Positive setback

## Slide 77: Figure 124.46 (b) Negative setback

## Slide 78: Figure 124.47 Cradle placement affects setback

## Slide 79: Animation: Wheel Alignment: Setback (The animation will automatically start in a few seconds)

## Slide 80: THRUST ANGLE
Thrust angle is the angle of the rear wheels as determined by the total rear toe.
The total of the rear toe setting determines the thrust line, or the direction the rear wheels are pointed.

## Slide 81: Figure 124.48 (a) Zero thrust angle

## Slide 82: Figure 124.48 (b) Thrust line to the right

## Slide 83: Figure 124.48 (c) Thrust line to the left

## Slide 84: Animation: Wheel Alignment: Thrust Angle (The animation will automatically start in a few seconds)

## Slide 85: TRACKING
The rear wheels should track directly behind the front wheels.
If the vehicle has been involved in an accident, it is possible that the frame or rear axle mounting could cause dog tracking.
Dog tracking is an alignment condition that is caused by having the rear wheel toe angles out of line with the front wheels causing the vehicle to travel slightly sideways.

## Slide 86: Figure 124.49 (a) Proper tracking

## Slide 87: Figure 124.49 (b) Front wheels steering toward thrust line

## Slide 88: Animation: Wheel Alignment: Track (The animation will automatically start in a few seconds)

## Slide 89: FOUR-WHEEL ALIGNMENT
Four-wheel alignment refers to the checking and/or adjustment of all four wheels.
Four-wheel alignment is important for proper handling and tire wear.

## Slide 90: Video Links (Internet Access Required)
Alignment angles (time 2:56)
Alignment (time 2:12)
Steering angles part 1 (time 17:34)
Steering angles part 2 (time 26:05)
Wheel alignment (time 2:41)
Caster (time 1:14)
Camber (time 5:16)
Camber action (time 0:54)
Alignment importance (time 4:01)
Camber (time 1:37)

## Slide 91: Video Links (Internet Access Required)
Alignment (time 3:16)
Ackerman steering (time 3:44)
Steering axis inclination (time 2:33)
Caster (time 2:15)
Alignment (time 8:41)
Alignment (time 4:01)
Vehicle handling (time 20:17)
Toe in (time 5:00)

## Slide 92: Copyright