## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 127
Manual Transmissions/ Transaxles
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
127.1 Discuss the need for a transmission.
127.2 Explain the different types of gears and gear ratios.
127.3 Describe the relationship between torque, speed, and power.
127.4 Describe the construction of a transmission.
127.5 Describe the torque flow through a manual transmission.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
127.6 Describe speed gears.
127.7 Explain the construction and operation of a synchronizer.
127.8 Describe the torque flow through a five-speed manual transmission.
127.9 Describe the procedure to diagnose, remove, disassemble, and install manual transmission/transaxle.

## Slide 4: THE NEED FOR A TRANSMISSION
A vehicle requires a lot of torque to start off and to climb hills, yet it does not require as much torque to move on level ground.
Using gears allows the engine speed to increase at low vehicle speeds yet still permits the engine speed to drop at higher speeds to save fuel and reduce exhaust emissions.

## Slide 5: GEAR TYPES (1 OF 2)
Spur Gear
  A spur gear consists of a gear blank with straight-cut teeth around its entire circumference.
Helical Gear
  A helical gear, although similar to a spur gear, has its teeth cut at an angle to the axis of the gear.
External Gears
  Gear teeth on their outside circumference

## Slide 6: GEAR TYPES (2 OF 2)
Internal Ring Gears
  Gears having teeth along the inside circumference.
Bevel Gears
  The teeth of a bevel gear are cut at an angle to the outside gear surface.
Hypoid Gears
  Hypoid gear sets have gear teeth that are curved much like the teeth of a spiral bevel gear.

## Slide 7: Figure 127.1 Spur gears have straight-cut teeth

## Slide 8: Figure 127.2 The teeth of a helical gear are cut at an angle to the gear axis

## Slide 9: Figure 127.3 A spur gear has straight-cut teeth. This design is very strong and is used where strength is important. Spur gears are noisy during operation. Helical-cut gears, on the other hand, operate quietly but create a force in line with the axis of the gears due to the angle of the gear teeth

## Slide 10: Figure 127.4 A pinion gear meshed with an internal ring gear rotates in the same direction around a parallel axis of rotation

## Slide 11: Animation: Internal & External Gear (The animation will automatically start in a few seconds)

## Slide 12: Figure 127.5 When two external gears mesh, they rotate in opposite directions

## Slide 13: Figure 127.6 Bevel gears are often used to change the direction of rotation and are typically used in differentials

## Slide 14: Figure 127.7 A differential uses a hypoid gear set to provide a change in the direction of torque and for gear reduction (torque increases) to the drive wheels

## Slide 15: GEAR RATIOS (1 OF 3)
Gear ratio is expressed as the number of rotations the drive gear must make in order to rotate the driven gear through one revolution.
Gear ratios, which are expressed relative to the number one, fall into three categories:
  Direct drive
  Gear reduction
  Overdrive

## Slide 16: GEAR RATIOS (2 OF 3)
Direct Drive
  If two meshed gears are the same size and have the same number of teeth, they will turn at the same speed.
Gear Reduction
  If one gear drives a second gear that has three times the number of teeth, the smaller drive gear must travel three complete revolutions in order to drive the larger gear through one rotation.

## Slide 17: GEAR RATIOS (3 OF 3)
Overdrive
  Overdrive is the opposite of a gear reduction condition and occurs when a driven gear turns faster than its drive gear.
Idler Gears
  A gear that operates between the drive and driven gears is called a floating gear, or idler gear.
  Idler gears affect direction of rotation not the speed of the gear.

## Slide 18: Figure 127.8 Gear ratio is determined by dividing the number of teeth of the driven (output) gear (24 teeth) by the number of teeth on the driving (input) gear (12 teeth). The ratio illustrated is 2:1

## Slide 19: Animation: External Gears: 2:1 (The animation will automatically start in a few seconds)

## Slide 20: Figure 127.9 This gear combination provides a gear reduction of 3:1

## Slide 21: Figure 127.10 This gear combination provides an overdrive ratio of 0.33:1

## Slide 22: Figure 127.11 Idler gears affect the direction of rotation in a gear train, but not the final drive ratio

## Slide 23: Animation: External Gears with Idler (The animation will automatically start in a few seconds)

## Slide 24: QUESTION 1: ?
In an overdrive gear ratio what is the relationship between the drive and driven gear?

## Slide 25: ANSWER 1:
The driven gear turns faster than its drive gear.

## Slide 26: TOEQUE, SPEED, AND POWER
Gears apply torque much like a wrench does; each tooth of a gear is actually a lever.
Torque and Speed Relationship
  Torque and speed have an inverse relationship: as one goes up, the other goes down.
Torque Multiplication
  Levers can be used to increase or multiply torque.
  Either distance or speed must always be given up in order to increase, or multiply, torque.

## Slide 27: Figure 127.12 Gears apply torque in the same way a wrench applies torque—the force applied multiplied by the distance from the center of the gear equals the torque

## Slide 28: Figure 127.13 A lever can be used to multiply torque, but it does so at the expense of distance or speed

## Slide 29: TRANSMISSION CONSTRUCTION (1 OF 2)
A transmission is usually constructed of cast aluminum.
The front of the transmission attaches to a separate bell housing.
At the front of the transmission (toward the engine) is the front bearing retainer.
The rear of the transmission usually includes a separate casting called the extension housing.

## Slide 30: TRANSMISSION CONSTRUCTION (2 OF 2)
The center housing is usually referred to as the transmission case.
The input shaft is splined to the clutch disc and is also referred to as the main gear, clutch gear, or main drive pinion assembly.
The main shaft, also called the output shaft.
All manual transmissions/transaxles use a countershaft.

## Slide 31: Figure 127.14 Cross section of a five-speed manual transmission showing the main parts

## Slide 32: FREQUENTLY ASKED QUESTION

## Slide 33: Figure 127.15 The torque capacity of a transmission is determined by the size of the gear and bearings used. The greater the distance, usually measured in millimeters such as 77 mm, between the main shaft and the countershaft, the greater the torque capacity

## Slide 34: Animation: Transmission Power Flow (The animation will automatically start in a few seconds)

## Slide 35: TORQUE FLOW THROUGH A MANUAL TRANSMISSION
The engine torque is applied to the input shaft when the clutch is engaged (clutch pedal up).
This torque is applied to the main gear.
The engine torque is multiplied by the ratio difference between the main gear and the cluster gear.
The engine torque then is applied to the drive wheels through the driveshaft, differential, and drive axles.

## Slide 36: SPEED GEARS
The gears on the main shaft are free to move on the shaft and are connected to the main shaft through the synchronizer hub when a shift is made.
The gears that rotate on the main shaft are called speed gears and are free to rotate on a film of oil or on bearings.

## Slide 37: Figure 127.16 Notice that the countershaft and the main shaft both use gears of increasing size that mesh together

## Slide 38: SYNCHRONIZER PARTS AND OPERATION (1 OF 2)
Interlocks either in the shifter linkage itself or inside the transmission/transaxle prevent selecting two gears at the same time.
Synchronizers are used in manual transmissions/transaxles to make shifting easier.
To synchronize means to make two or more events occur at the same time.
The synchronizer ensures the two gears to be meshed must be rotating at the same speed.

## Slide 39: SYNCHRONIZER PARTS AND OPERATION (2 OF 2)
Synchronizer Construction
  Although there are a number of design variations, all are similar and include a hub, a sliding sleeve, a blocker ring, (or stop ring or synchronizer ring), keys, and springs.
Synchronizer Operation
  When a force on the sleeve that moves it toward the speed gear. The sleeve and the inserts contact the stop ring (blocking ring). The synchronizer ring (stop ring) engages the cone on the speed gear, causing both assemblies to reach the same speed.

## Slide 40: Figure 127.17 A typical shift mechanism is designed to not only give the driver a solid feel when shifting, but also prevents shifting into reverse except from the neutral position

## Slide 41: Figure 127.18 When a shift is made, the sleeve is moved toward the speed gear. The sleeve presses the stop ring against the cone area of the speed gear. The friction between the stop ring and the speed gear causes the speed of the two to become equal, permitting the sleeve to engage the gear clutch teeth of the speed gear.

## Slide 42: Figure 127.19 Typical synchronizer assembly

## Slide 43: Animation: Check Blocker Ring Clearance (The animation will automatically start in a few seconds)

## Slide 44: Figure 127.20 Synchronizer keys are attached to the clutch hub and push against the synchronizer ring when the sleeve is being moved during a shift. Notice the grooves on the synchronizer ring. These grooves prevent lubricating oil from becoming trapped between the ring and the cone surface of the speed gear.

## Slide 45: Figure 127.21 A shift sequence starts when the shift fork applies a force on the sleeve that moves it toward the speed gear. (2) The sleeve and the inserts contact the stop ring. (3) The synchronizer ring engages the cone on the speed gear, causing both assemblies to reach the same speed. (4)

## Slide 46: Animation: Synchronizer Operation (The animation will automatically start in a few seconds)

## Slide 47: Figure 127.22 Before reassembling the transmission/transaxle, carefully inspect the splines on the synchronizer sleeves for wear. The shape of the splines helps prevent the transmission/transaxle from jumping out of gear during acceleration and deceleration

## Slide 48: Figure 127.23 Exploded view of a triple-cone synchronizer. The inner and outer rings rotate with the synchronizer sleeve while the middle ring rotates with the speed gear

## Slide 49: QUESTION 2: ?
What is the purpose of the synchronizer?

## Slide 50: ANSWER 2:
The synchronizer ensures the two gears to be meshed must be rotating at the same speed.

## Slide 51: FIVE SPEED TRANSMISSION TORQUE FLOW (1 OF 3)
Neutral
  All of the synchronizer sleeves are centered on their hubs.
First Gear
  In first gear, the shift linkage slides the 1–2 synchronizer sleeve rearward toward the first speed gear.
Second Gear
  In second gear, the shift linkage slides the 1–2 synchronizer sleeve forward, away from the first speed gear and toward the second speed gear.

## Slide 52: FIVE SPEED TRANSMISSION TORQUE FLOW (2 OF 3)
Third Gear
  In third gear, the shift linkage centers the 1–2 synchronizer sleeve and moves the 3–4 synchronizer sleeve back toward the third speed gear.
Fourth Gear
  In fourth gear, the shift linkage moves the 3–4 synchronizer sleeve forward, away from the third speed gear and toward the input shaft drive gear.

## Slide 53: FIVE SPEED TRANSMISSION TORQUE FLOW (3 OF 3)
Fifth Gear
  In fifth gear, the shift linkage centers the 3–4 synchronizer sleeve and moves the fifth synchronizer sleeve toward the fifth speed gear.
Reverse
  There are two common reverse gear designs used on transmissions:
  Sliding gear
  Constant-mesh gear

## Slide 54: Figure 127.24 In neutral, the input shaft and the countershaft are rotating if the clutch is engaged (clutch pedal up), but no torque is being transmitted through the transmission

## Slide 55: Figure 127.25 In first gear, the 1–2 synchronizer sleeve is moved rearward, locking the first speed gear to the output shaft. Torque is transmitted from the input shaft to the countershaft and then to the output shaft

## Slide 56: Animation: 5-Speed Transmission, 1st Gear (The animation will automatically start in a few seconds)

## Slide 57: Figure 127.26 In second gear, the 1–2 synchronizer sleeve is moved forward, which locks the second speed gear to the output shaft

## Slide 58: Animation: 5-Speed Transmission, 2nd Gear (The animation will automatically start in a few seconds)

## Slide 59: Figure 127.27 To achieve third gear, the shaft linkage first centers the 1–2 synchronizer sleeve and then moves the 3–4 synchronizer sleeve rearward, locking third speed gear to the output shaft

## Slide 60: Animation: 5-Speed Transmission, 3rd Gear (The animation will automatically start in a few seconds)

## Slide 61: Figure 127.28 In fourth gear, the 3–4 synchronizer sleeve is moved forward, which locks the fourth speed gear to the output shaft

## Slide 62: Animation: 5-Speed Transmission, 4th Gear (The animation will automatically start in a few seconds)

## Slide 63: Figure 127.29 To achieve fifth gear, the shift linkage first centers the 3–4 synchronizer sleeve and then moves the fifth synchronizer sleeve toward the fifth speed gear, locking it to the output shaft

## Slide 64: Animation: 5-speed Transmission: 5th Gear (The animation will automatically start in a few seconds)

## Slide 65: Figure 127.30 Torque flows through the transmission in reverse gear. Note that the idler gear drives the 1–2 synchronizer sleeve gear, which is splined to the output shaft

## Slide 66: Animation: Transmission: Reverse (The animation will automatically start in a few seconds)

## Slide 67: Figure 127.31 Cutaway of a T56 six-speed transmission showing all of its internal parts

## Slide 68: Animation: 6-Speed Transaxle Operation (The animation will automatically start in a few seconds)

## Slide 69: MANUAL TRANSAXLE CONSTRUCTION
Most transaxles use speed gears and synchronizers on both the input and output shafts.
The differential assembly, also called a final drive assembly, attaches to the output shaft and splits the torque to both front drive axles.

## Slide 70: Figure 127.32 Notice that this five-speed transaxle from a Dodge/Plymouth Neon uses synchronizers on both the input and output shafts

## Slide 71: Figure 127.33 Cutaway of a typical manual transaxle showing all of its internal parts including the final drive assembly

## Slide 72: Animation: Power Transfer Unit (The animation will automatically start in a few seconds)

## Slide 73: Animation: Transaxle Power Flow (The animation will automatically start in a few seconds)

## Slide 74: Animation: Transaxle: 1st Gear (The animation will automatically start in a few seconds)

## Slide 75: Animation: Transaxle, 2nd Gear (The animation will automatically start in a few seconds)

## Slide 76: Animation: Transaxle, 3rd Gear (The animation will automatically start in a few seconds)

## Slide 77: Animation: Transaxle, 4th Gear (The animation will automatically start in a few seconds)

## Slide 78: Animation: Transaxle, 5th Gear (The animation will automatically start in a few seconds)

## Slide 79: Animation: Transaxle, Final Drive (The animation will automatically start in a few seconds)

## Slide 80: Animation: Transaxle, Reverse (The animation will automatically start in a few seconds)

## Slide 81: TRANSMISSION/ TRANSAXLE REMOVAL
Disconnecting the negative battery cable.
Safely hoisting and supporting the vehicle.
Supporting the engine with a holding fixture or other support (front-wheel-drive).
Remove the drive axle shafts or drive shaft (rear-wheel-drive).
Remove the clutch linkage and shift linkage.
Disconnect the vehicle speed sensor and reverse (backup) light connectors.
Remove the attaching bolts/nuts from the engine and transmission/transaxle mounts and then removing the unit from the vehicle.

## Slide 82: Figure 127.34 Most front-wheel-drive (FWD) vehicles require the use of a fixture to support the engine before removing the transaxle

## Slide 83: Figure 127.35 A transaxle being removed from underneath a vehicle and being supported by a transmission jack

## Slide 84: Figure 127.36 Typical cable-operated shift linkage used on a front-wheel-drive transaxle

## Slide 85: TRANSMISSION/ TRANSAXLE DISASSEMBLY
Before disassembling the transmission/transaxle, drain any remaining gear lubricant from the unit and dispose of it properly.
Mount the transmission/transaxle on a holding fixture or place it on a large, clean work surface.
Check the service manual for the exact disassembly procedures to follow for the unit being serviced.

## Slide 86: Figure 127.37 Drain the fluid into a suitable container and dispose of the old fluid according to local, state, and federal regulations

## Slide 87: Figure 127.38 A Borg-Warner T5 five-speed transmission shown with the shifter cover removed

## Slide 88: Figure 127.39 The cost to replace these gears may exceed the cost of a replacement transmission

## Slide 89: Figure 127.40 It often requires two people to assemble a transaxle because the shaft with the shifter forks needs to be placed into the case as an assembly, as on this unit

## Slide 90: Figure 127.41 (a) During the disassembly of any manual transmission/transaxle, carefully check for the location of the snap rings. Often they are hidden. Consult the factory service manual or unit repair manual for information and procedures for the unit being serviced

## Slide 91: Figure 127.41 (b) Using snap-ring pliers to remove a snap ring. Many snap rings have an “up” side. Be sure to reinstall any snap rings in the correct direction

## Slide 92: Figure 127.41 (c) After the snap ring is removed, some components can be simply lifted off the main shaft, while other gears may require the use of a press

## Slide 93: Figure 127.42 (a) When a ball bearing is pressed off a shaft, the bearing should be supported by the inner race (if possible) so the force is not exerted on the outer race by the balls

## Slide 94: Figure 127.42 (b) Use caution when pressing parts onto the main shaft. Always follow the specified assembly procedures as found in service information

## Slide 95: Figure 127.43 The dial indicator is set up to measure input shaft endplay as it is lifted and dropped using the pry bar

## Slide 96: HARD-TO-SHIFT PROBLEM DIAGNOSIS
Several items that could be worn or defective can cause a manual transmission/transaxle to be difficult to shift, including:
  Clutch not fully disengaging.
  Worn synchronizer.
  Worn, cracked, or loose shift forks.
  Excessive input- or main-shaft end play.
  Improper lubrication.

## Slide 97: GEAR LUBRICATION
After the installation of the transmission/transaxle, the unit should be filled with the correct lubricant.
  SAE 80W-90 (GL-4) gear lube
  STF (synchromesh transmission fluid), but with friction characteristics designed for manual transmissions.
  ATF (automatic transmission fluid)
  Engine oil (usually SAE 5W-30)

## Slide 98: Figure 127.44 Some manual transmissions/transaxles require synchromesh transmission fluid

## Slide 99: NV 1500 MANUAL TRANSMISSION SERVICE

## Slide 100: 1 A NV-1500 five-speed manual transmission is used in two-wheel drive applications only.

## Slide 101: 2 The shifter assembly has been removed. Note the roll pin in the center of the shift lever socket.

## Slide 102: 3 Snap-ring pliers are being used to remove the snap ring retaining the input shaft bearing.

## Slide 103: 4 The upside down case is being separated showing the countershaft (top) and shift forks.

## Slide 104: 5 Before further disassembly can be accomplished, the shift lever socket roll pin must be driven out using a punch and a hammer.

## Slide 105: 6 The shift shaft and forks can now be removed.

## Slide 106: 7 The reverse idle gear is unbolted from the case and removed.

## Slide 107: 8 The output shaft assembly fifth gear (far left) and the synchronizer assemblies.

## Slide 108: 9 The bearing is being removed using a bearing splitter and a hydraulic press.

## Slide 109: 10 A speed gear (bottom) along with the double row needle bearing used between the shaft and the speed gear. The hub (center) is splined and rotates with the output shaft.

## Slide 110: 11 A synchronizer assembly being reassembled. It often takes several hands to hold the hub (center) and the sleeve (outer ring).

## Slide 111: 12 A hydraulic press is used to reassemble output shaft and bearing.

## Slide 112: 13 The assembled output shaft is held against the counter shaft to double check that all of the gears have been correctly assembled.

## Slide 113: 14 The assembled output shaft and counter shaft are being reinstalled in the transmission case.

## Slide 114: 15 The case halves are bolted together.

## Slide 115: 16 The last step is to assembly the shift lever and check for proper operation in all gear positions.

## Slide 116: NV-350 TRANSAXLE SERVICE

## Slide 117: 1 After the transaxle has been removed from the vehicle and the fluid drained, place the transaxle on a work surface.

## Slide 118: 2 The bell housing case half containing the large output shaft front bearing (center) and the input shaft front bearing (smaller bearing on the left).

## Slide 119: 3 The differential assembly is simply lifted out of half of the case.

## Slide 120: 4 The input and output shafts are a press fit into the bearings and are also retained with a snap ring, which must be removed.

## Slide 121: 5 Using a special tool, the input and output shafts are pressed out of the housing using a hydraulic press.

## Slide 122: 6 The input shaft can be disassembled using a bearing splitter and a press, or two screwdrivers to pry the gears off the shaft.

## Slide 123: 7 This transaxle uses both brass and powdered metal synchronizer rings with a fiber (paper) inner cone surface.

## Slide 124: 8 Synchronizer ring gaps are being measured using a feeler (thickness) gauge. The factory specifications are usually 0.040 to 0.069 inches.

## Slide 125: 9 The gear clutch teeth should be inspected for wear.

## Slide 126: 10 An assembled synchronizer assembly containing a sleeve, keys, springs, and detent.

## Slide 127: 11 The input shaft (left) and the output shaft (right) are checked for proper assembly before being installed into the case.

## Slide 128: 12 The differential bearing preload is determined by measuring for zero end play; then adding the thickness shim under the bearing cup.

## Slide 129: 13 The bearing cup is being installed using an installation tool and a hammer.

## Slide 130: 14 All of the shift forks and shift arms must be aligned properly before installing the components into the case.

## Slide 131: 15 All of the components, including the differential (right), the output shaft (center), and the input shaft (left), plus the shift linkage are installed and checked for proper positioning.

## Slide 132: 16 The case halves being reinstalled. The bearings (top) must be pressed back onto the input and output shafts using a press.

## Slide 133: 17 The bell housing case being reattached.

## Slide 134: 18 The completed assembly. Notice the bearing cover (top) has already been installed.

## Slide 135: Video Links (Internet Access Required)
How synchronizers work (time 13:11)
Clutch and trans operation (time 3:30)
Manual trans operation (time 0:43)
Manual trans power flow (time 0:13)
Trans operation (time 7:59)
Trans operation (time 2:19)
Manual trans animation (time 0:43)
Manual overdrive transmission (time 2:40)
Electronic manual transmission (time 0:49)
Overdrive transmission old British car (time 1:34)

## Slide 136: Video Links (Internet Access Required)
AX-15 teardown part 1 (time 13:57)
AX-15 assembly part 2 (time 10:43)
AX-15 rebuild part 3 (time 19:46)
AX-15 rebuild part 4 (time 13:32)
AX-15 rebuild part 5 (time 25:27)
AX-15 rebuild part 6 (time 22:14)
AX-15 rebuild part 7 (time 9:28)
Shifter bushing repair (time 3:23)
Gearshift knob removal (time 1:23)
Transmission noise (time 3:04)

## Slide 137: Video Links (Internet Access Required)
Transaxle noise (time 1:15)
Drivetrain diagnosis (time 1:11)
Honda manual transmission fluid change (time 10:20)

## Slide 138: Copyright