## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 41
Series, Parallel, and Series-Parallel Circuits
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
41.1 Identify a series circuit.
41.2 State Kirchhoff’s voltage law and calculate voltage drops in a series circuit.
41.3 Explain series circuit laws.
41.4 Identify a parallel circuit.
41.5 State Kirchhoff’s current law.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
41.6 Calculate the total resistance in a parallel circuit.
41.7 Identify a series-parallel circuit.
41.8 Calculate the total resistance of a series-parallel circuit.
41.9 Prepare for ASE Electrical/Electronic Systems (A6) certification test content area “A” (General Electrical/Electronic System Diagnosis).

## Slide 4: SERIES CIRCUIT
A series circuit is a complete circuit that has more than one electrical load where all of the current has only one path to flow through all of the loads.
The circuit must be continuous or have continuity in order for current to flow through the circuit.

## Slide 5: OHM’S LAW AND SERIES CIRCUITS
Because all current flows through all resistances, the total resistance is the sum (addition) of all resistances.
Ohm’s law can be used to calculate the value of one unknown (voltage, resistance, or amperes) if the other two values are known.

## Slide 6: Figure 41.1 A series circuit with three bulbs. All current flows through all resistances (bulbs). The total resistance of the circuit is the sum of the total resistance of the bulbs.

## Slide 7: Figure 41.2 A series circuit with two bulbs

## Slide 8: Animation: Math Formula Circuit Resistance (The animation will automatically start in a few seconds)

## Slide 9: KIRCHHOFF’S VOLTAGE LAW
Kirchhoff’s Second Law
  The voltage around any closed circuit is equal to the sum (total) of the voltage drops across the resistances.
Applying Kirchhoff’s Law
  The voltage drop can be determined by using Ohm’s law and calculating for voltage (E) using the value of each resistance individually:

## Slide 10: Figure 41.3 As current flows through a circuit, the voltage drops in proportion to the amount of resistance in the circuit. Most, if not all, of the resistance should occur across the load, such as the bulb in this circuit.

## Slide 11: Figure 41.4 In a series circuit, the voltage is dropped or lowered by each resistance in the circuit. The higher the resistance, the greater the drop in voltage

## Slide 12: Figure 41.5 A voltmeter reads the differences of voltage between the test leads. The voltage read across a resistance is the voltage drop that occurs when current flows through a resistance.

## Slide 13: FREQUENTLY ASKED QUESTION

## Slide 14: QUESTION 1: ?
What is Kirchhoff’s voltage law?

## Slide 15: ANSWER 1:
  The voltage around any closed circuit is equal to the sum (total) of the voltage drops across the resistances.

## Slide 16: SERIES CIRCUIT LAWS
Law 1
  The total resistance in a series circuit is the sum total of the individual resistances.
Law 2
  The current is constant throughout the entire circuit.
Law 3
  Although the current is constant, the voltage drops across each resistance in the circuit. The voltage drop across each load is proportional to the value of the resistance compared to the total resistance.

## Slide 17: Figure 41.6 In this series circuit with a 2-ohm resistor and a 4-ohm resistor, current (2 amperes) is the same throughout, even though the voltage drops across each resistor

## Slide 18: SERIES CIRCUIT EXAMPLES
Each of the four examples discussed includes solving for the following:
  Total resistance in the circuit
  Current flow (amperes) through the circuit
  Voltage drop across each resistance

## Slide 19: Figure 41.7 Example 1

## Slide 20: Figure 41.8 Example 2

## Slide 21: Figure 41.9 Example 3

## Slide 22: Figure 41.10 Example 4

## Slide 23: Animation: Series Circuit, Open (The animation will automatically start in a few seconds)

## Slide 24: PARALLEL CIRCUITS
A parallel circuit is a complete circuit that has more than one path for the current.
The separate paths that split and meet at junction points are called branches, legs, or shunts.
The current flow through each branch or leg varies, depending on the resistance in that branch.

## Slide 25: Animation: Parallel Circuit (The animation will automatically start in a few seconds)

## Slide 26: KIRCHHOFF’S CURRENT LAW
Kirchhoff’s Current Law
  The current flowing into any junction of an electrical circuit is equal to the current flowing out of that junction.

## Slide 27: Figure 41.11 The amount of current flowing into junction point A equals the total amount of current flowing out of the junction

## Slide 28: PARALELL CIRCUIT LAWS
Law 1
  The total resistance of a parallel circuit is always less than that of the smallest-resistance leg.
Law 2
  The voltage is the same for each leg of a parallel circuit.
Law 3
  The sum of the individual currents in each leg equals the total current.

## Slide 29: Animation: Parallel Circuit Law 2 (The animation will automatically start in a few seconds)

## Slide 30: Figure 41.12 The current in a parallel circuit splits (divides) according to the resistance in each branch

## Slide 31: Animation: Parallel Circuit Law 3 (The animation will automatically start in a few seconds)

## Slide 32: DETERMINING TOTAL RESISTANCE IN A PARALLEL CIRCUIT (1 OF 2)
Method 1
  The total current (in amperes) can be calculated first by treating each leg of the parallel circuit as a simple circuit.
Method 2
  If only two resistors are connected in parallel, the total resistance (RT) can be found using the formula RT = (R1 *R2)/(R1 + R2).

## Slide 33: DETERMINING TOTAL RESISTANCE IN A PARALLEL CIRCUIT (2 OF 2)
Method 3
  A formula that can be used to find the total resistance for any number of resistances in parallel is 1/RT = 1/R1 +1/R2 + 1/R3 + . . .
Method 4
  This method uses an electronic calculator, commonly available at very low cost.
Method 5
  This method can be easily used whenever two or more resistances connected in parallel are of the same value.

## Slide 34: Figure 41.13 In a typical parallel circuit, each resistance has power and ground, and each leg operates independently of the other legs of the circuit

## Slide 35: Figure 41.14 A schematic showing two resistors in parallel connected to a 12-volt battery

## Slide 36: Figure 41.15 A parallel circuit with three resistors connected to a 12-volt battery

## Slide 37: Figure 41.16 Using an electronic calculator to determine the total resistance of a parallel circuit

## Slide 38: Figure 41.17 Another example of how to use an electronic calculator to determine the total resistance of a parallel circuit. The answer is 13.45 ohms.

## Slide 39: Animation: Parallel Circuit Law 1 (The animation will automatically start in a few seconds)

## Slide 40: Figure 41.18 When a circuit has more than one resistor of equal value, the total resistance can be determined by simply dividing the value of the resistance (12 ohms in this example) by the number of equal-value resistors (4 in this example) to get 3 ohms

## Slide 41: PARALLEL CIRCUIT EXAMPLES
Each of the four examples discussed includes solving for the following:
  Total resistance
  Current flow (amperes) through each branch, as well as total current flow
  Voltage drop across each resistance

## Slide 42: Figure 41.19 Example 1

## Slide 43: Figure 41.20 Example 2

## Slide 44: Figure 41.21 Example 3

## Slide 45: Figure 41.22 Example 4

## Slide 46: Animation: Parallel Circuit, Volts (The animation will automatically start in a few seconds)

## Slide 47: Animation: Parallel Circuit, Open (The animation will automatically start in a few seconds)

## Slide 48: QUESTION 2: ?
Why is the total resistance of a parallel circuit less than the
smallest resistance?

## Slide 49: ANSWER 2:
With many branches, more current can flow from the battery

## Slide 50: SERIES-PARALLEL CIRCUITS
Series-parallel circuits are a combination of series and parallel segments in one complex circuit.
There are two basic types of series-parallel circuits.
  A circuit where the load is in series with other loads in parallel.
  A circuit where a parallel circuit contains resistors or loads that are in series with one or more branches.

## Slide 51: Figure 41.23 A series-parallel circuit

## Slide 52: SOLVING SERIES-PARALLEL CIRCUIT PROBLEMS
The key to solving series-parallel circuit problems is to combine or simplify as much as possible.
For example, if there are two loads or resistances in series within a parallel branch or leg, then the circuit can be made simpler if the two are first added together before attempting to solve the parallel section.

## Slide 53: Figure 41.24 Solving a series-parallel circuit problem

## Slide 54: SERIES-PARALLEL CIRCUIT EXAMPLES
Each of the four examples discussed includes solving for the following:
  Total resistance
  Current flow (amperes) through each branch, as well as total current flow
  Voltage drop across each resistance

## Slide 55: Figure 41.25 Example 1

## Slide 56: Figure 41.26 Example 2

## Slide 57: Figure 41.27 Example 3

## Slide 58: Figure 41.28 Example 4

## Slide 59: QUESTION 3: ?
What would be the effect of an open circuit in a series portion
of a series-parallel circuit?

## Slide 60: ANSWER 3:
It would affect the entire circuit.

## Slide 61: Video Links (Internet Access Required)
Series Circuits (time 7:11)
Intro the Parallel Circuits (time 5:43)
Calculating Current in a Parallel Circuit (time 11:00)
Solving Series-Parallel Circuits (time 8:03)
Series-Parallel Circuits (time 2:42)

## Slide 62: Copyright