## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 72
Ignition System Diagnosis and Service
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES (1 of 2)
72.1 Describe the procedure used to check for spark.
72.2 Diagnose ignition system-related problems.
72.3 Inspect and test ignition coils, magnetic sensors, and Hall-effect sensors.
72.4 Discuss what to inspect and look for during a visual inspection of the ignition system.
72.5 Describe how to test for poor performance and for a no-start condition.

## Slide 3: LEARNING OBJECTIVES (2 of 2)
72.6 Explain how to verify the distributor position.
72.7 Inspect and test secondary ignition system circuit and components.
72.8 Discuss the purpose and function of ignition timing and spark advance.
72.9 Describe how to test the ignition system using an oscilloscope.
72.10 This chapter will help prepare for Engine Repair (A8) ASE certification test content area “B” (Ignition System Diagnosis and Repair).

## Slide 4: CHECKING FOR SPARK
In the event of a no-start condition, check for secondary voltage out of the ignition coil or to the spark plugs.
Install a spark tester, and crank the engine.
Typical causes of a no-spark (intermittent spark) condition include the following:
  Weak ignition coil, low or no voltage to coil, open coil wire or plug, defective pickup coil and defective module.

## Slide 5: Figure 72.1 A spark tester looks like a regular spark plug with an alligator clip attached to the shell. This tester has a specified gap that requires at least 25,000 volts (25 kV) to fire

## Slide 6: Figure 72.2 A close-up showing the recessed center electrode on a spark tester. It is recessed 3/8 inch into the shell and the spark must then jump another 3/8 inch to the shell for a total gap of 3/4 inch

## Slide 7: QUESTION 1: ?
Why should a spark tester be used to check for spark, rather than a standard spark plug?

## Slide 8: ANSWER 1:
The spark must jump across a larger gap to more effectively test the system.

## Slide 9: ELECTRONIC IGNITION TROUBLESHOOTING PROCEDURE
Turn the ignition on (engine off) and, using either a voltmeter or a test light, test for battery voltage available at the positive terminal of the ignition coil.
Connect the voltmeter or test light to the negative side of the coil and crank the engine. The voltmeter should fluctuate or the test light should blink, indicating that the primary coil current is being turned on and off.

## Slide 10: IGNITION COIL TESTING USING AN OHMMETER
To test the primary coil winding resistance:
  Set the meter to read low ohms.
  Measure the resistance between the positive terminal and the negative terminal of the ignition coil.
To test the secondary coil winding resistance:
  Set the meter to read kilohms (kΩ).
  Measure the resistance between either primary terminal and the secondary coil tower.

## Slide 11: Figure 72.3 (a) Set the digital meter to read ohms and measure between the two primary terminals of the coil. Most coils are less than one ohm

## Slide 12: Figure 72.3 (b) To measure the secondary winding, connect one meter lead to one of the primary terminals and the other to the secondary terminal

## Slide 13: TESTING MAGNETIC SENSORS
Magnetic sensors must be tested to see if they stick to iron or steel, indicating that the magnetic strength of the sensors is okay.
The sensor can be tested using a digital meter set to read AC volts.

## Slide 14: Figure 72.4 Measuring the resistance of a magnetic crankshaft position (CKP) sensor using an ohmmeter

## Slide 15: QUESTION 2: ?
How is a magnetic sensor tested for resistance and AC voltage output?

## Slide 16: ANSWER 2:
A digital multimeter can be used to measure resistance of the sensor and the AC voltage output.

## Slide 17: TESTING HALL-EFFECT SENSORS
Using a digital voltmeter, check for the presence of changing voltage (pulsed on and off or digital DC) when the engine is being cranked.
The best test is to use an oscilloscope and observe the waveform.

## Slide 18: Figure 72.5 A Hall Effect sensor produces a square waveform, whereas a magnetic sensor produces an analog waveform, when viewed on scope

## Slide 19: Tech Tip

## Slide 20: Figure 72.6 A track inside an ignition coil is not a short, but rather it is a low-resistance path or hole that has been burned through from the secondary wiring to the steel core

## Slide 21: TECH TIP

## Slide 22: Figure 72.7 If the coil is working, the end of the magnetic pickup tool moves with the changes in the magnetic field around the coil

## Slide 23: IGNITION SYSTEM DIAGNOSIS USING VISUAL INSPECTION
Check all spark plug wires for proper routing.
Check that all spark plug wires are securely attached.
Check that all spark plug wires are clean and free from excessive dirt or oil.
Remove the distributor cap and carefully check the cap and distributor rotor for faults.
Remove the spark plugs and check for excessive wear or other visible faults.

## Slide 24: TESTING FOR POOR PERFORMANCE
Many diagnostic equipment manufacturers offer methods for testing distributorless ignition systems on an oscilloscope.
A simple method of testing distributorless (waste-spark systems) ignition with the engine off involves removing the spark plug wires (or connectors) from the spark plugs (or coils or distributor cap) and installing short lengths (2 inches) of rubber vacuum hose in series.

## Slide 25: Figure 72.8 Using a vacuum hose and a grounded test light to ground one cylinder at a time on a DIS. This works on all types of ignition systems and provides a method for grounding out one cylinder at a time without fear of damaging any component.

## Slide 26: DISTRIBUTOR INDEXING
A few engines using a distributor also use it to house a camshaft position (CMP) sensor.
One purpose of this sensor is to properly initiate the fuel-injection sequence.
A miss-indexed distributor may cause: surging, light bucking, or intermittent engine misfire.
Always use the factory procedure as stated in service information to properly index the distributor.

## Slide 27: Figure 72.9 The relationship between the crankshaft position (CKP) sensor and the camshaft position (CMP) sensor is affected by wear in the timing gear and/or chain

## Slide 28: SECONDARY IGNITION INSPECTION
Distributor Cap and Rotor
  Inspect a distributor cap for cracks, carbon tracks, and corrosion.
COP and Waste Spark Inspection
  Look for evidence of carbon track or heat-related faults to the plug boot.
Spark Plug Wire Inspection
  Spark plug wires should be visually inspected for cuts or defective insulation and checked for resistance with an ohmmeter.

## Slide 29: Figure 72.10 When checking a coil-on-plug (COP) assembly, check that the primary and secondary wiring looks normal and that the coil is not discolored from arcing or corrosion

## Slide 30: Figure 72.11 When checking a waste spark-type ignition system, check that the secondary wires are attached to the correct coil terminal and that the wiring is correctly routed to help avoid cross-fire

## Slide 31: Figure 72.12 Corroded terminals on a waste-spark coil can cause misfire diagnostic trouble codes to be set

## Slide 32: Figure 72.13 This spark plug boot on an overhead camshaft engine has been arcing to the valve cover, causing a misfire to occur

## Slide 33: Figure 72.14 Measuring the resistance of a spark plug wire with a multimeter set to the ohms position. The reading of 16.03 kΩ (16.030 ohms) is okay because the wire is about 2-feet long. High-resistance spark plug wires can cause an engine misfire.

## Slide 34: Animation: Test Spark Plug Wire (The animation will automatically start in a few seconds)

## Slide 35: TECH TIP

## Slide 36: Figure 72.15 Spark plug wire boot pliers is a handy addition to any tool box

## Slide 37: TECH TIP

## Slide 38: Figure 72.16 Always take the time to install spark plug wires back into the original holding brackets (wiring combs)

## Slide 39: SPARK PLUG SERVICE
The Need for Service
  Spark plugs should be inspected and replaced every 20,000 to 100,000 miles depending on the vehicle.
Spark Plug Inspection
  Carbon fouling
  Oil fouling
  White coolant deposits
When installing spark plugs, always use the correct tightening torque.

## Slide 40: Figure 72.17 When removing spark plugs, it is wise to arrange them so that they can be compared and any problem can be identified with a particular cylinder

## Slide 41: Figure 72.18 A spark plug thread chaser is a low-cost tool that hopefully is not used often, but is necessary to use to clean the threads before new spark plugs are installed.

## Slide 42: Figure 72.19 Since 1991, General Motors engines have been equipped with slightly (1/8 inch or 3 mm) longer spark plugs. This requires that a longer spark plug socket be used to prevent the possibility of cracking a spark plug during installation.

## Slide 43: Figure 72.20 A normally worn spark plug that has a tapered platinum-tipped center electrode

## Slide 44: Figure 72.21 A worn spark plug showing fuel and/or oil deposits

## Slide 45: Figure 72.22 A spark plug from an engine that had a blown head gasket. The white deposits could be from the additives in the coolant.

## Slide 46: Figure 72.23 A platinum-tipped spark plug that is fuel soaked, indicating a fault with the fuel system or the ignition system causing the spark plug to not fire.

## Slide 47: QUICK AND EASY SECONDARY IGNITION TESTS
Following are some quick and easy secondary ignition tests:
  If any spark is visible or a “snapping” sound is heard, the location should be closely inspected and the defective parts replaced.
  For intermittent problems, use a spray bottle to apply a water mist to the spark plugs, distributor cap, and spark plug wires.

## Slide 48: Figure 72.24 A water spray bottle is an excellent diagnostic tool to help find an intermittent engine misfire caused by a break in a secondary ignition circuit component.

## Slide 49: IGNITION TIMING
Purpose
  Ignition timing refers to when the spark plug fires in relation to piston position.
Checking Ignition Timing
  To be assured of the proper ignition timing, follow exactly the timing procedure indicated on the underhood vehicle emission control information (VECI) decal.
The ignition timing cannot be adjusted on waste-spark and COP ignition systems.

## Slide 50: Figure 72.25 Typical timing marks. The numbers of the degrees are on the stationary plate and the notch is on the harmonic balancer

## Slide 51: Figure 72.26 The initial (base) timing is where the spark plug fires at idle speed. The PCM then advances the timing based primarily on engine speed

## Slide 52: Figure 72.27 (a) Typical SPOUT connector as used on many Ford engines equipped with distributor ignition (DI)

## Slide 53: Figure 72.27 (b) The connector must be opened (disconnected) to check and/or adjust the ignition timing. On DIS/EDIS systems, the connector is called SPOUT/SAW (spark output/spark angle word)

## Slide 54: SCOPE-TESTING THE IGNITION SYSTEM (1 OF 6)
Any automotive scope with the correct probes or adapters show an ignition system pattern.
Firing Line
  The leftmost vertical (upward) line is called the firing line.
Spark Line
  The spark line is a short horizontal line immediately after the firing line.

## Slide 55: SCOPE-TESTING THE IGNITION SYSTEM (2 OF 6)
Intermediate Oscillations
  The intermediate oscillations follow the spark line, and are also called the “ringing” of the coil as it is pulsed.
Transistor-On Point
  When the transistor turns on an electronic system, the coil is being charged.
Dwell Section
  Dwell is the amount of time that the current is charging the coil from the transistor-on point to the transistor-off point.

## Slide 56: SCOPE-TESTING THE IGNITION SYSTEM (3 OF 6)
Pattern Selection
  Superimposed
  Raster (stacked)
  Display (parade)
Reading the Scope on Display (Parade)
  The firing lines should all be 5 to 15 kV in height and be within 3 kV of each other.

## Slide 57: SCOPE-TESTING THE IGNITION SYSTEM (4 OF 6)
Reading the Spark Lines
  The spark lines should be level and one-fourth as high as the firing lines (1.5 to 2.5 kV, but usually less than 2 kV).
Spark Line Slope
  An upward-sloping spark line can indicate a lean air–fuel mixture.
  A downward sloping spark line is finding ground through deposits.

## Slide 58: SCOPE-TESTING THE IGNITION SYSTEM (5 OF 6)
Reading the Intermediate Section
  The intermediate section should have three or more oscillations (bumps) for a correctly operating ignition system.
Electronic Ignition and the Dwell Section
  Many EI systems also produce a “hump” in the dwell section, which reflects a current-limiting circuit in the control module.
Dwell Variation (Electronic Ignition)
  Typically caused by a worn mechanical component.

## Slide 59: SCOPE-TESTING THE IGNITION SYSTEM (6 OF 6)
Coil Polarity
  If the pattern is upside down, the primary wires on the coil may be reversed, causing the coil polarity to be reversed.
Acceleration Check
  All firing lines should rise evenly
  If the firing lines on one or more cylinders fail to rise, this indicates fouled spark plugs.
Rotor Gap Voltage
  The normal rotor gap voltage is 3 to 7 kV

## Slide 60: Figure 72.28 Typical engine analyzer hookup that includes a scope display. (1) Coil wire on top of the distributor cap if integral type of coil; (2) number 1 spark plug connection; (3) negative side of the ignition coil; (4) ground (negative) connection of the battery

## Slide 61: Figure 72.29 Clip-on adapters are used with an ignition system that uses an integral ignition coil

## Slide 62: Figure 72.30 Typical secondary ignition oscilloscope pattern

## Slide 63: Figure 72.31 A single cylinder is shown at the top and a four cylinder engine at the bottom

## Slide 64: Figure 72.32 Drawing shows what is occurring electrically at each part of the scope pattern

## Slide 65: Figure 72.33 Typical secondary ignition pattern. Note the lack of firing lines on superimposed pattern

## Slide 66: Figure 72.34 Raster is the best scope position to view the spark lines of all the cylinders to check for differences. Most scopes display the cylinder 1 at the bottom. The other cylinders are positioned by firing order above cylinder 1

## Slide 67: Figure 72.35 Display is the only position to view the firing lines of all cylinders. Cylinder 1 is displayed on the left (except for its firing line, which is shown on the right). The cylinders are displayed from left to right by firing order

## Slide 68: Figure 72.36 A downward-sloping spark line usually indicates high secondary ignition system resistance or an excessively rich air–fuel mixture

## Slide 69: Figure 72.37 An upward-sloping spark line usually indicates a mechanical engine problem or a lean air–fuel mixture

## Slide 70: Figure 72.38 The relationship between the height of the firing line and length of the spark line can be illustrated using a rope. Because energy cannot be destroyed, the stored energy in an ignition coil must dissipate totally, regardless of engine operating conditions

## Slide 71: QUESTION 3: ?
What are the sections of a secondary ignition scope pattern?

## Slide 72: ANSWER 3:
Firing line, spark line, intermediate section, and dwell section.

## Slide 73: SCOPE TESTING A WASTE-SPARK IGNITION SYSTEM
A handheld digital storage oscilloscope can be used to check the pattern of each individual cylinder.
Some larger scopes are able to display both power and waste-spark waveforms.
Because the waste spark does not require as high a voltage level as the cylinder on the power stroke, the waste form is normally lower.

## Slide 74: Figure 72.39 A dual-trace scope pattern showing both the power and the waste spark from the same coil (cylinders 1 and 6). Note that the firing line is higher on the cylinder that is under compression (power); otherwise, both patterns are almost identical

## Slide 75: SCOPE-TESTING A COIL-ON-PLUG IGNITION SYSTEM
Each individual coil can be shown on a scope and, using the proper cables and adapters.
Always follow the scope equipment manufacturer’s instructions.
Normal ignition patterns may vary based on manufacturer system designs.

## Slide 76: Figure 72.40 A secondary waveform of a Ford 4.6 liter V-8, showing three sparks occurring at idle speed

## Slide 77: Video Links (Internet Access Required)
NGC ignition codes (time 4:21)
Crank no start (time 6:15)
Distributor installation (time 2:34)
Coil testing (time 14:39)
COP misfire diagnosis (time 11:01)
Spark plug thread repair (time 6:55)
Ignition fault codes (time 10:00)
Check for spark (time 1:58)
Distributor cap and rotor (time 2:57)
Spark plugs (time 3:25)

## Slide 78: Video Links (Internet Access Required)
Ignition coil (time 3:40)
Setting ignition timing (time 1:44)
Spark plug tube repair (time 7:08)
Finding an ignition voltage leak (time 6:28)
Misfire diagnosis (time 8:12)
Subaru no spark (time 13:25)
Ignition system primary testing (time 5:04)
Scanning to detect misfires (time 5:03)
Spark plugs (time 6:56)
Spark plug replacement (time 3:11)

## Slide 79: Video Links (Internet Access Required)
Ignition coil (time 0:53)
Crankshaft position sensor (time 3:55)
Crankshaft position sensor (time 4:07)
P0340 and P0341 (time 3:44)
Crankshaft position sensor (time 3:32)
Crankshaft sensor (time 9:57)
Nissan cam sensor fault (time 4:16)
Crankshaft sensor (time 5:12)
Scope testing a crankshaft sensor (time 6:47)
Cam sensor circuit test (time 1:02)

## Slide 80: Video Links (Internet Access Required)
Chrysler hall effect sensor testing part 1 (time 14:55)
Chrysler hall effect sensor testing part 2 (time 6:10)
Knock sensor testing (time 16:09)
Camshaft sensor (time 6:59)
VRS bypass testing (time 6:15)
Testing crankshaft sensors (time 4:39)
Testing crankshaft sensors (time 5:00)
Camshaft position sensor testing (time 2:43)
Cam sensor (time 8:57)
Camshaft timing (time 4:09)

## Slide 81: Video Links (Internet Access Required)
Install cam bearings (time 2:24)
Ignition triggers (time 1:03)
Ignition control module (time 1:02)
Transformers (time 0:49)
IAC test with a scope (time 7:17)
COP ignition system (time 3:00)
Misfire diagnosis (time 11:38)
How to change spark plugs and ignition coil (time 13:37)
Replacing a distributor cap (time 2:11)
Basic tune up for a car or truck (time 23:09)

## Slide 82: Video Links (Internet Access Required)
How to find a misfire when a scanner isn’t any help (time 2:41)
How to check ignition spark (time 2:23)

## Slide 83: Copyright