## Slide 1: Automotive Technology Principles, Diagnosis, and Service
Sixth Edition
Chapter 86
Exhaust Gas Recirculation System
Copyright © 2018, 2015, 2011 Pearson Education, Inc. All Rights Reserved

## Slide 2: LEARNING OBJECTIVES
86.1 Discuss the purpose and function of exhaust gas recirculation (EGR) systems.
86.2 Explain the strategies to monitor onboard diagnostics generation II (OBD-II) exhaust gas recirculation (EGR) systems.
86.3 Explain how to diagnose a defective EGR system.

## Slide 3: EXHUAT GAS RECIRCULATION SYSTEMS (1 OF 5)
Introduction
  Exhaust gas recirculation (EGR) is an emission control system that lowers the amount of nitrogen oxides (NOx) formed during combustion.
NOx Formation
  Nitrogen (N2) and oxygen (O2) molecules bond to form NOx (NO, NO2) when combustion flame front temperatures exceed 2,500°F (1,370°C).

## Slide 4: EXHUAT GAS RECIRCULATION SYSTEMS (2 OF 5)
Controlling NOx
  The EGR system routes small quantities, usually between 6% and 10%, of exhaust gas into the intake manifold.
  The result is a lower peak combustion temperature.
EGR System Operation
  Typically only used when the engine is above idle.
  Not used at idle, during warm-up, and at wide-open throttle.

## Slide 5: EXHUAT GAS RECIRCULATION SYSTEMS (3 OF 5)
Positive and Negative Back Pressure EGR Valves
  Positive back pressure EGR valves require a positive back pressure in the exhaust system.
  Negative back pressure EGR valves react to a low-pressure pulse created by the exhaust valve, by closing a small internal valve, which allows the EGR valve to be opened by vacuum.
Computer Controlled EGR Systems
  Most vehicles today use the powertrain control module (PCM) to operate the EGR system.

## Slide 6: EXHUAT GAS RECIRCULATION SYSTEMS (4 OF 5)
EGR Valve Position Sensors
  A linear potentiometer on the top of the EGR valve stem indicates valve position to the PCM.
Digital EGR Valves
  The digital EGR valve consists of three solenoids controlled by the powertrain control module (PCM).
  Each solenoid controls a different size orifice in the base.
  It can produce any of seven different flow rates.

## Slide 7: EXHUAT GAS RECIRCULATION SYSTEMS (5 OF 5)
Linear EGR
  A linear EGR valve contains a pulse-width modulated solenoid to precisely regulate exhaust gas flow and a feedback potentiometer that signals the PCM regarding the actual position of the valve.

## Slide 8: Figure 86.1 Nitrogen oxides (NOx) create a red-brown haze that often hangs over major cities

## Slide 9: Figure 86.2 When the EGR valve opens, the exhaust gases flow through the valve and into passages in the intake manifold

## Slide 10: Figure 86.3 Back pressure in the exhaust system is used to close the control valve, allowing engine vacuum to open the EGR valve

## Slide 11: Figure 86.4 Typical vacuum-operated EGR valve. The operation of the valve is controlled by the PCM by pulsing the EGR control solenoid on and off

## Slide 12: Figure 86.5 An EGR valve position sensor on top of an EGR valve

## Slide 13: Figure 86.6 Digital EGR valve as used on some older General Motors engines

## Slide 14: Figure 86.7 A General Motors linear EGR valve

## Slide 15: Figure 86.8 The EGR valve pintle is pulse-width modulated and a three-wire potentiometer provides pintle-position information back to the PCM

## Slide 16: QUESTION 1: ?
What is the purpose of an EGR system?

## Slide 17: ANSWER 1:
To reduce combustion temperatures and lower NOx tailpipe emissions.

## Slide 18: OBD-II EGR MONITORING STRATEGIES
Purpose and Function
  The PCM monitors the system and alerts the driver and the technician if an emission system is malfunctioning.
Monitoring Strategies
  Some vehicle manufacturers, such as Chrysler, monitor the difference in the exhaust oxygen sensor’s voltage activity as the EGR valve opens and closes.
  Most Fords use an EGR monitor test sensor called a delta pressure feedback EGR (DPFE) sensor.
  Many vehicle manufacturers use the manifold absolute pressure(MAP) sensor as the EGR monitor on some applications.

## Slide 19: Figure 86.9 A typical Ford DPFE sensor and related components

## Slide 20: Animation: Exhaust Gas Recirculation, EGR (The animation will automatically start in a few seconds)

## Slide 21: Figure 86.10 An OBD-II active test. The PCM opens the EGR valve and then monitors the MAP sensor and/or engine speed (RPM) to verify that it meets acceptable values

## Slide 22: DIAGNOSING A DEFECTIVE EGR SYSTEM (1 OF 2)
Symptoms
  Detonation (spark knock or ping) during acceleration or during cruise (steady-speed driving)
  Excessive oxides of nitrogen (NOx) exhaust emissions
  Rough idle or frequent stalling
  Poor performance/low power, especially at low engine speed

## Slide 23: DIAGNOSING A DEFECTIVE EGR SYSTEM (2 OF 2)
EGR Testing Procedures
  Check the vacuum diaphragm of the EGR valve to see if it can hold vacuum.
  Apply vacuum from a hand-operated vacuum pump and check for proper operation.
  Monitor engine vacuum drop.

## Slide 24: Tech Tip

## Slide 25: Figure 86.11 Removing the EGR passage plugs from the intake manifold on a Honda

## Slide 26: EGR RELATED OBD-II DIAGNOSTIC TROUBLE CODES

## Slide 27: QUESTION 2: ?
What are the symptoms of a defective EGR system?

## Slide 28: ANSWER 2:
Rough idle, spark knock, poor performance, and frequent stalling.

## Slide 29: Video Links (Internet Access Required)
EGR valve (time 0:45)
EGR port cleaning (time 5:13)
Ford DPFE sensor (time 4:31)
EGR position sensor (time 1:43)
EGR pintle position sensor (time 1:57)
EGR diagnostics (time 4:30)
EGR inspection and testing (time 17:12)
EGR temperature sensor (time 0:50)
Scanning EGR valve perimeter (time 2:18)
EGR temp sensor (time 0:50)
EGR system (time 2:08)

## Slide 30: Copyright