## Slide 1: Advanced Engine Performance Diagnosis
Seventh Edition
Chapter 23
Gasoline Direct-injection Systems
Copyright © 2020 Pearson Education, Inc. All Rights Reserved

## Slide 2: Figure 23.1 A comparison of a port fuel injection system (right) to a gasoline direct injection system on the left

## Slide 3: Figure 23.2 A gasoline direct-injection system injects fuel under high pressure directly into the combustion chamber

## Slide 4: Figure 23.3 A G D I system uses a low-pressure pump in the gas tank similar to other types of fuel-injection systems. The P C M controls the pressure of the high-pressure pump using sensor inputs

## Slide 5: Figure 23.4 A typical direct-injection system uses two pumps—one low-pressure electric pump in the fuel tank and the other a high-pressure pump driven by the camshaft. The high pressure fuel system operates at a pressure as low as 500 P S I during light load conditions and as high as 2,900 P S I under heavy loads

## Slide 6: Animation: Direct Fuel Injection, Mechanical ((Animation will automatically start in a few seconds)he animation will automatically start in a few seconds)

## Slide 7: Figure 23.5a A typical camshaft-driven high-pressure pump used to increase fuel pressure to 2,000 P S I or higher

## Slide 8: Figure 23.5b The high-pressure pump assembly removed from the engine. Many G D I engines use a roller where the high-pressure pump rides against the cam lobes to help reduce friction and wear

## Slide 9: Figure 23.6 A gasoline direct-injection (G D I) fuel rail and pump assembly with the electric pressure control valve

## Slide 10: Figure 23.7 Notice that there are conditions when the port fuel-injector, located in the intake manifold, and the gasoline direct injector, located in the cylinder, both operate to provide the proper air–fuel mixture

## Slide 11: Figure 23.8 In this design, the fuel injector is at the top of the cylinder and sprays fuel into the cavity of the piston

## Slide 12: Figure 23.9 The side injector combines with the shape of the piston to create a swirl as the piston moves up on the compression stroke

## Slide 13: Figure 23.10 The piston creates a tumbling force as it moves upward

## Slide 14: Figure 23.11 There may become a driveability issue because the gasoline direct-injection injector is exposed to combustion carbon and fuel residue

## Slide 15: Figure 23.12 The high-pressure lines use a ball and socket connection. The ball end deforms when the line is tightened and must be replaced with a new part whenever it is removed

## Slide 16: Figure 23.13 Whenever a G D I fuel injector is removed, a new Teflon seal must be installed to ensure a leak-free connection in the combustion chamber

## Slide 17: Video Links (Internet Access Required)
Gasoline direct injection (time 5:50)
Bosch Gasoline Direct Injection System (time 6:20)
Accelerator pedal position sensor testing (time 3:22)
Accelerator pedal position sensor (time 5:35)
Electronic throttle (time 4:15)

## Slide 18: Copyright