## Slide 1: Automotive Heating And Air Conditioning
Eighth Edition
Chapter 8
Cooling System Operation and Diagnosis

## Slide 2: Learning Objectives (1 of 2)
8.1 Explain the purpose and function of the cooling system and cooling system operation.
8.2 Explain the purpose of thermostats, radiators, pressure caps, and water pumps.
8.3 Explain coolant flow in the engine and coolant recovery systems.

## Slide 3: Learning Objectives (2 of 2)
8.4 Explain the purpose of cooling fans and heater cores.
8.5 Describe cooling system testing and explain the purpose of the coolant temperature warning light.
8.6 Explain cooling system inspection and cooling system service.

## Slide 4: Cooling System
Coolant flows through the engine, where it picks up heat.
It then flows to the radiator, where the heat is given up to the outside air.
The coolant continually recirculates through the cooling system.

## Slide 5: FIGURE 8–1 Typical combustion and exhaust temperatures.

## Slide 6: Cooling System Operation (1 of 2)
Its temperature rises as much as 15°F (8°C) as it goes through the engine; then it recools as it goes through the radiator.
The coolant flow rate may be as high as 1 gallon (4 liters) per minute for each horsepower the engine produces.

## Slide 7: FIGURE 8–3 Coolant flow through a typical engine cooling system.

## Slide 8: Cooling System Operation (2 of 2)
Hot coolant comes out of the thermostat housing on the top of the engine.
The engine coolant outlet is connected to the top of the radiator by the upper hose and clamps.
The coolant in the radiator is cooled by air flowing through the radiator.

## Slide 9: Thermostats (1 of 2)
There is a normal operating temperature range between low-temperature and high-temperature extremes.
The thermostat controls the minimum normal temperature.
The thermostat is a temperature-controlled valve placed at the engine coolant outlet.

## Slide 10: Thermostats (2 of 2)
An encapsulated, wax-based, plastic-pellet heat sensor is located on the engine side of the thermostatic valve.
As the engine warms, heat swells the heat sensor.

## Slide 11: FIGURE 8–5 (a) When the engine is cold, the coolant flows through the bypass. (b) When the thermostat opens, the coolant can flow to the radiator.

## Slide 12: Animation: Thermostat Operation (The animation will automatically start in a few seconds)

## Slide 13: Radiators
What are the types of radiators?
What are the two basic designs of radiators?
How radiators work

## Slide 14: FIGURE 8–11 The tubes and fins of the radiator core.

## Slide 15: Pressure Cap
The filler neck is fitted with a pressure cap.
The cap has a spring-loaded valve that closes the cooling system vent.
This causes cooling pressure to build up to the pressure setting of the cap.
At this point, the valve will release the excess pressure to prevent system damage.

## Slide 16: Animation: Radiator Pressure Cap (The animation will automatically start in a few seconds)

## Slide 17: FIGURE 8–14 The pressure valve maintains the system pressure and allows excess pressure to vent. The vacuum valve allows coolant to return to the system from the recovery tank.

## Slide 18: Coolant Recovery Systems
What is the purpose and function of coolant recover systems?
  Most cooling systems connect the overflow to a plastic reservoir to hold excess coolant while the system is hot.
Surge tank
  Some vehicles use a surge tank, which is located at the highest level of the cooling system and holds about 1 quart (1 liter) of coolant.

## Slide 19: FIGURE 8–15 The level in the coolant recovery system raises and lowers with engine temperature.

## Slide 20: Water Pumps
Water pumps are not positive displacement pumps.
The water pump is a centrifugal pump that can move a large volume of coolant without increasing the pressure of the coolant.
Coolant leaving the pump impeller is fed through a scroll.

## Slide 21: Animation: Water Pump Operation (The animation will automatically start in a few seconds)

## Slide 22: FIGURE 8–19 This severely corroded water pump could not circulate enough coolant to keep the engine cool. As a result, the engine overheated and blew a head gasket.

## Slide 23: Coolant Flow in the Engine
Coolant flows through the engine in one of the following ways:
  Parallel flow system
  Series flow system
  Series–parallel flow system
Excess pressure usually forces some coolant from the system through an overflow.

## Slide 24: Animation: Coolant Flow-World Engine (The animation will automatically start in a few seconds)

## Slide 25: FIGURE 8–22 A Chevrolet V-8 block that shows the large coolant holes and the smaller gas vent or bleed holes that must match the head gasket when the engine is assembled.

## Slide 26: Cooling Fans (1 of 2)
The thermostatic spring operates a valve that allows the fan to freewheel when the radiator is cold.
As the radiator warms to about 150°F (65°C), the air hitting the thermostatic spring will cause the spring to change its shape.

## Slide 27: Cooling Fans (2 of 2)
The thermal fan is designed so that it uses little power at high engine speeds and minimizes noise.
A second type of thermal fan has a thermostatic spring added to the silicone coupling fan drive.
The thermal fan has a silicone coupling fan drive mounted between the drive pulley and the fan.

## Slide 28: FIGURE 8–23 A typical electric cooling fan assembly showing the radiator and related components.

## Slide 29: Heater Cores
Most of the heat absorbed from the engine by the cooling system is wasted.
Some of this heat, however, is recovered by the vehicle heater.
The heater and air conditioning work in series to maintain vehicle compartment temperature.

## Slide 30: FIGURE 8–25 A typical heater core installed in a heating, ventilation, and air-conditioning (HVAC) housing assembly.

## Slide 31: Cooling System Testing and Warning Light (1 of 2)
Many cooling system faults can be found by performing a thorough visual inspection.
Pressure testing using a hand operated pressure tester is a quick and easy cooling system test.
Check for fluorescent dye in the coolant to check for a leak, one that is specifically designed for coolant.

## Slide 32: Cooling System Testing and Warning Light (2 of 2)
Most vehicles are equipped with a heat sensor for the engine operating temperature indicator light.
  If the warning light comes on during driving (or the temperature gauge goes into the red danger zone), then the coolant temperature is about 250°F to 258°F (120°C to 126°C), which is still below the boiling point of the coolant

## Slide 33: Animation: Warning Lights, Engine Coolant Temperature (The animation will automatically start in a few seconds)

## Slide 34: FIGURE 8–29 Use dye specifically made for coolant when checking for leaks using a black light.

## Slide 35: FIGURE 8–30 When an engine overheats, often the coolant overflow container boils.

## Slide 36: Cooling System Inspection and Cooling System Service (1 of 2)
Normal maintenance involves an occasional check on the coolant level.
Testing if belt tension is within factory specifications:
  Belt tension gauge; marks on the tensioner; torque wrench reading; deflection

## Slide 37: Cooling System Inspection and Cooling System Service (2 of 2)
Flushing coolant
Coolant exchange machine
Hose inspection
Disposing of used coolant
Cleaning the radiator exterior

## Slide 38: Animation: Changing Coolant (The animation will automatically start in a few seconds)

## Slide 39: Animation: Pressure Test Cooling System (The animation will automatically start in a few seconds)

## Slide 40: FIGURE 8–31 Typical marks on an accessory drive belt tensioner.

## Slide 41: FIGURE 8–32 (a) Many vehicle manufacturers recommend that the bleeder valve be opened whenever refilling the cooling system. (b) Chrysler recommends that a clear plastic hose (1/4 inch ID) be attached to the bleeder valve and directed into a suitable container to keep from spilling coolant onto the ground and on the engine and to allow the technician to observe the flow of coolant for any remaining air bubbles.

## Slide 42: Summary (1 of 3)
The purpose and function of the cooling system is to maintain proper engine operating temperature.
The thermostat controls engine coolant temperature by opening at its rated opening temperature to allow coolant to flow through the radiator.

## Slide 43: Summary (2 of 3)
Coolant fans are designed to draw air through the radiator to aid in the heat transfer process, drawing the heat from the coolant and transferring it to the outside air through the radiator.
The cooling system should be tested for leaks using a hand-operated pressure pump.

## Slide 44: Summary (3 of 3)
Water pumps are usually engine driven and circulate coolant through the engine and the radiator when the thermostat opens.
Coolant flows through the radiator hoses to and from the engine and through heater hoses to send heated coolant to the heater core in the passenger compartment.

## Slide 45: Video Links (Internet Access Required)
HVAC mode door (time 17:07)
Heater stuck on defrost (time 4:57)
Air duct cleaning (time 4:35)
Blower motor replacement (time 7:15)
Blower not blowing air (time 3:46)
Blend air door motor (time 3:49)
Blower motor replacement (time 6:59)
Blower motor (time 4:01)
Kia cabin air filter (time 2:11)
Subaru cabin air filter (time 3:54)

## Slide 46: Video Links (Internet Access Required)
Ford Fusion cabin air filter (time 2:11)
Camaro cabin air filter (time 2:58)