## Slide 1
By Jim Halderman

## Slide 2: Introduction
Jim Halderman
Former flat-rate technician
Author and former automotive instructor
jim@jameshalderman.com

## Slide 3
Download this presentation
www.JamesHalderman.com

## Slide 4
Diagnosis of the battery, starting and charging systems from the driver's seat.
Using an OBD II breakout box (BOB).
How to check DTCs, monitor status and scan tool data all from the driver’s seat.
Test drive.
Topics to be Discussed

## Slide 5
What do you think could be checked from the driver's seat?
Oil level?
Battery voltage?
Starter/ alternator issues?
Air conditioning condition?
Diagnosis?
Today All or Mostly Electrical

## Slide 6
Customer stated that he had to pound on dash to get the car to start.
Yep. the customer pounded on the dash,
So hard that the needles fell off.
Verify Customer Concern

## Slide 7
Check the following:
Lights, turn signal, and horn
Windshield wipers and washers
All accessories
Use mirrors in the shop to see the lights
Visual Inspection

## Slide 8
My Shop Mirror

## Slide 9
If the cruise control is inoperative,
Could be due to inoperative brake lights or CHMSL.
Check them by looking through the rearview mirror, using the mirrors in the shop.
TECH TIP

## Slide 10: Visual Inspection
According to General Motors, 20% of faults are found using visual inspection
Ask students to perform a visual inspection.
Typical bugs: Remove the dipstick; Turn MAF backwartds

## Slide 11
2018+ GM use a QR code on the “B” pillar.
When using a QR reader on a smartphone or scan tool camera, shows the VIN and the “Regular Production Option” (RPO) codes. (2016-2017 VIN only)
Needed for the right parts and diagnosis.
Service Information – GM RPO Codes

## Slide 12
Check everything that does and does not work, including:
Test the brake pedal feel.
Check for proper engagement into drive and reverse.
If the vehicle moves forward and back, but does not shift, it is usually the valve body.
If the vehicle does not move, usually the unit needs to be removed.
Where to Start?

## Slide 13
Any Dash Warning Lights On?

## Slide 14
Green = Information
Amber = Caution
Red = Warning
Dash Symbol Chart
www.JamesHalderman.com

## Slide 15
Dash Warning Lights Mean?
(Electronic Throttle control fault detected)

## Slide 16
Old school
Under the hood
New school
From the driver’s seat
Checking Oil Level

## Slide 17
Since 2010, Jaguar uses an ultrasonic oil level sensor.
It uses sound waves that bounce off the oil surface and then displays the oil level.
Scroll through trip settings, using the trip button on the end of the turn signal stalk.
Ultrasonic Oil Level Sensor

## Slide 18
Oil level displayed on the dash is mostly on European vehicles at this this time, including:
Jaguar
BMW
Mercedes
Audi (Audi A8 shown)
Oil Level Dash Displays

## Slide 19
ATF? - Some vehicles
Tire Pressure? - Most vehicles
What else can be measured from the driver’s seat?

## Slide 20
Ford Mustang Variable Effort Steering
Changeable from the driver’s seat

## Slide 21
Is the air conditioning working as designed?
Measure vent temperature and look at outside temperature.
A/C Diagnosis from the Driver’s Seat

## Slide 22
Airflow Check

## Slide 23
Complaint - There is an “electrical short” because the driver gets shocked when touching the door handle when leaving the car.
Cause - Driver’s movement on the upholstery caused a static charge buildup.
Correction - Used static guard spray on the seats.
Case Study

## Slide 24
Buick LaCrosse 3.8 L
Complaint - Customer states that the battery goes dead overnight.
Customer says that a “humming” sound is heard from under the dash.
Case Study

## Slide 25
Used a thermal image camera (FLIR) to locate which module was powered up all the time.
The HVAC module was not shutting down.
It was controlled by the BCM.
Replaced BCM and programmed the unit.
Case Study - Solution

## Slide 26
Voltage Display

## Slide 27
DC voltage (cranking and charging voltage)
AC voltage (AC ripple voltage)
Used to determine the condition of the following:
  Battery SOC
  Starter
  Alternator
Electrical Measurements from the Driver’s Seat

## Slide 28
Where is the DLC?

## Slide 29
OBD II Plug - Pins #4 and #5 are longer.
Why?
OBD II Connector

## Slide 30
Because the ground touches first when making the connection.
Helps prevent voltage spikes.
OBD II Connector

## Slide 31
Compliant - On a Chevrolet Avalanche, the scan tool would not power up.
Cause - No 12 volts at pin #16 of the DLC. Found a blown fuse for the lighter (power socket).
(Customer remembered hearing a “pop” when he plugged in a device to the power outlet.)
Correction - Replaced the that fuse feeds pin #16 of the DLC.
Case Study

## Slide 32
Use OBD II male connector…Pin #4 (-) and #16 (+) go to power plug and to a jump box.
OBD II DLC Memory Saver

## Slide 33
Use a break-out box (BOB) and a DMM.
Connect the Meter to the Terminals 4 and 16 of the DLC
Checking Voltage at the DLC

## Slide 34
Pin 16: Red LED lights up when there is power.
Pins 4 and 5: Green LED's on each pin light up when ground is good.
Pins 2, 6, 7, 10: Yellow LED's on each pin light up to identify vehicle data OBD-II protocol and activity.
LEDs on the OBD II BOB

## Slide 35
Where to Purchase a Break-Out Box (BOB)

## Slide 36
Add a breakout box or a DLC extension harness to every vehicle.
Protects the DLC from damage from students trying to plug in a scan tool.
A breakout box makes it easy to check for voltages without doing any harm to the vehicle.
Tech Tip

## Slide 37
Battery Testing-
Connect and watch the voltmeter and turn on high beam headlights.
Watch voltage drop.
After it stabilizes, turn off the lights.
Watch how fast the voltage increases.
The final voltage is the SOC.
Battery Voltage

## Slide 38
Battery voltage should be 12.6 V or higher.
Battery Condition Test

## Slide 39
Cranking voltage -
Crank the engine.
Observe the battery voltage.
It should be above 9.6 Volts during cranking.
Cranking System Voltage

## Slide 40
Complaint – Chevy Equinox infotainment system rebooting on occasion when starting the engine.
Cause – Voltage briefly dropping too low while cranking.
Captured by Fluke 87 using the peak min/max feature (250 µSec capture rate).
Correction – Replacing the battery corrected the problem.
Case Study

## Slide 41
Charging Voltage -
Start the engine and observe the voltmeter.
It should be 13.5-15.0 Volts.
Charging System Voltage

## Slide 42
Complaint - Ford F-150 speedometer needle went up and down with engine speed, rather than vehicle speed.
Cause - Excessive AC Ripple voltage (over 1 volt AC) at the battery.
Correction - Replacing the alternator restored the proper operation of the speedometer.
Case Study

## Slide 43
Complaint - The owner of a Chevrolet Silverado (6.6L diesel V8) stated that the battery warning light would come on when accelerating hard. Retrieved a C0800 DTC (system voltage is greater than 16 volts).
Cause - The charging voltage was measured at 17.7 volts.
Correction - The alternator was replaced, the DTC was cleared, and the vehicle returned to the customer.
Case Study

## Slide 44
AC Ripple Voltage –
Start the engine.
Turn on the headlights to provide an electrical load.
Switch the meter to read AC volts.
Meter should read less than 0.5 Volt.
Ripple Voltage Testing

## Slide 45
Connect scope leads to terminals #4 and #16 at the DLC.
Hold the accelerator pedal to the floor to enter “clear flood” mode.
Crank the engine and observe the waveform.
Relative Power Balance Test

## Slide 46
Anything already plugged into the DLC?

## Slide 47
Because the device is plugged into the DLC, it has power (#16) and ground (#4) at all times.
Can cause some driveability issues and false DTCs.
Can result in no savings. (Driving late at night because of a flight from the west coast, for example.)
Insurance Telematics

## Slide 48
The PCM, of course, monitors all functions.
Can transmit “state of health” messages to the vehicle manufacturer (i.e. On Star).
Diagnosis Telematics

## Slide 49
Smart Phone Interface – Chevrolet Volt

## Slide 50
OBD DLC Wiring

## Slide 51
CAN Terminating Resistors

## Slide 52
Terminating Resistance Testing
(Two 120 ohm in parallel – 60 Ohms)

## Slide 53
Stop-Start Systems

## Slide 54
This means that a DTC has been stored.
Check for stored DTCs.
Then check TSBs.
Follow service information.
Check Engine Light On?

## Slide 55
Check DTCs
Diagnosing OBD II DTCs

## Slide 56
Cadillac CTS
Complaint: Check engine light on and stumble on acceleration at times.
Cause: Code P0101 Check PIDs with an Autolink scanner. (Mass air flow sensor out of range.)
Correction - Replaced MAF.
Case Study

## Slide 57
Before starting the engine, connect the scan tool.
Four types of scan tools:
Code readers
OBD II global (generic)
Factory scan tool
Enhanced aftermarket scan tool.
Scan Tool

## Slide 58
Code Readers
(Usually cost less than $100)

## Slide 59
Uses a smart phone Bluetooth adapter (usually less than $20).
Purchase a phone app (about $5.00).
IOS: OBD Car Doctor, E OBD2
Android: OBD Car Doctor, Torque, EOBD2, Dash Command
Third-party apps may need to pay to get full function.
Smart Phone Scan Tool

## Slide 60
OBD II Global (Generic) Scan Tools

## Slide 61
Enhanced Aftermarket Scan Tools

## Slide 62
Factory Scan Tools

## Slide 63
Some scan tool technology is built into the vehicle.
Cars like the Hyundai Genesis include a “System Check” visual that pops up in the center of the gauge cluster at start-up.
2016+ Hyundai Genesis

## Slide 64
Scan Tool Data (PIDs)
(Perform all Module Scan)

## Slide 65: Cylinder Contribution Test
Such as provided by the Ford IDS scan tool.
Cylinder Contribution Test

## Slide 66
P0300 etc.
Use the scan tool to do the hard work from the driver’s seat.
Look at the misfire data.
P0300 Random Misfire DTC

## Slide 67
Some scan tools can show misfire data or use Mode $06.
Misfire Data

## Slide 68: Global OBD II Modes
Mode $01 — Request live data
Mode $02—Request freeze frame information
Mode $03 – Request Stored Trouble Codes
Mode $04—Clear/reset emissions-related diagnostic information
Mode $05—Request oxygen sensor test results
Mode $06—Request on-board monitoring test results for specific monitored systems
Mode $07 — Request emission-related diagnostic trouble codes detected during current or last completed driving cycle
Mode $08—Request control of on-board system, test or component
Mode $09—Request vehicle information
Mode $0A (10)—Request emissions-related diagnostic trouble codes with permanent status after a clear/reset emission-related diagnostic information service.

## Slide 69
Global OBD II was designed for engineers to check the operation of non-continuously monitored systems.
It was not intended to be used by service technicians.
Mode $06 is used by service technicians to monitor the PCM test results of various systems.
Mode $06 is used to maintain all noncontinuous monitors and pending DTCs.
Mode $06

## Slide 70
Check Monitor Status

## Slide 71
Rough Idle
Surge
No Codes
What data PID indicates the problem?
Case Study
(1997 Chevy Truck 350 V8)

## Slide 72
Rough Idle
Surge
No Codes
What data PID indicates the problem?
Case Study
(1997 Chevy Truck 350 V8)

## Slide 73
Camshaft Wear
Causing the CMP Retard (-6 degrees)

## Slide 74
A factory or an enhanced aftermarket scan tool allows the technician to:
Turn on individual lights
Operate individual power windows and other accessories that are connected to the BUS system.
Bi-Directional Control

## Slide 75
The engine RPM signal comes from the CPK sensor.
As the number goes up, the engine is going faster.
This is usually the most important input.
High Authority Inputs

## Slide 76
Look Carefully at All PIDs

## Slide 77
On a cold engine -
Key on/Engine off (KOEO) and look at the values for ECT (engine coolant temperature) and IAT (intake air temperature).
Basically, the same sensor and the two temperatures should agree.
ECT = IAT

## Slide 78
The ECT sensor has a higher authority than the IAT and is therefore more likely to be the cause of a starting or cold running problem.
The ECT is the only sensor used by the PCM when the ignition key is first turned from on to start.
ECT = IAT (continued)

## Slide 79
A MAP sensor is a high-authority sensor, especially on speed density-controlled engines.
The MAP reading at KOEO should be atmospheric pressure (about 29.50 in. Hg.), depending on altitude and weather conditions.
An easier value to remember is that it should be about 4.6- 4.8 volts.
MAP = BARO

## Slide 80
The MAP sensor is basically a vacuum gauge connected to the intake manifold.
Can be used to monitor basic engine health such as:
Retarded cam timing (low steady vacuum)
Restricted exhaust (vacuum drops at higher engine speeds)
MAP vs. Vacuum

## Slide 81
Long-term fuel trim (LTFT) can add or subtract more fuel than STFT.
LTFT is slower than STFT.
The purpose of LTFT is to keep STFT within plus or minus 10%.
Long Term/Short Term Fuel Trim

## Slide 82
I suggest that you ignore STFT.
STFT is what is happening this instant.
LTFT gives a history of the exhaust mixture and is more helpful when it comes to a diagnosis.
Add the two together to get the total amount of added or subtracted fuel.
LTFT = +8%, STFT = -3%, total = +5%.
LTFT and STFT Diagnosis

## Slide 83
Look for a vacuum leak.
Look for a cracked exhaust manifold.
+LTFT Too High

## Slide 84
LTFT = +12%
STFT = +2%
How is the engine running now?
Fuel Trim Example

## Slide 85
Answer:
  The engine is operating normally now because the PCM has compensated for a slightly lean air-fuel mixture by increasing the injector pulse-width.
  Look for a vacuum leak or low fuel pressure.
Fuel Trim Example

## Slide 86
Test Drive the Vehicle

## Slide 87
Volumetric efficiency (VE) is the percentage of air entering the engine compared to the theoretical airflow.
Typical normally aspirated engines will test having a VE of 75% to 90%.
Older two-valve cylinder head engines will test lower than newer engines equipped with four valves per cylinder.
Percentages above 100% are possible on supercharged or turbocharged engines.
Volumetric Efficiency

## Slide 88
Must Maintain at least 850mV

## Slide 89
Accelerate -
If O2 goes low, the fuel system is lean.
Check for MAF reporting error, clogged fuel filter, or weak fuel pump.
If O2 goes high, something is restricted. Check intake and exhaust.
Power Test Drive

## Slide 90
O2 High -
BARO PID stays steady. Exhaust system is restricted.
O2 High -
BARO PID ratchets down. Intake is restricted.
Test Drive - continued

## Slide 91
An everyday repair.
Most replacement modules require programming.
Current hardware and subscription access is a must.
Advantages to both generic and manufacturer specific J2534 pass through devices.
Module Programming

## Slide 92
Item | Yes | No | Maybe
Warning lights | X |  | 
A/C Vent temperature | X |  | 
Tire pressure | X (most vehicles) |  | 
Steering wheel effort | X (some vehicles) |  | 
Battery testing | X |  | 
Oil level |  |  | X
Starter Amp testing |  | X | 
Starting/charging testing | X (several tests) |  | 
DLC protocol activity | X |  | 
CAN Resistance | X |  | 
Head and brake lights | X |  | 
Scan tool data | X |  | 
Diagnose restricted intake | X |  | 
Diagnose restricted exhaust | X |  | 
Summary Chart

## Slide 93
Cars in the Future?

## Slide 94
There are many systems that can be checked and diagnosed from the driver’s seat.
Think easy.
Think flat-rate.
Think fast diagnosis.
Get to the root cause quickly.
Fix the car right the first time.
Customer satisfaction
Summary

## Slide 95
Website

## Slide 96
Textbooks

## Slide 97
Jim Halderman
Contact Information
Jim@JamesHalderman.com