Cooling System Tests

Meets ASE Task:  (A1-D-1)  P-1  Identify and interpret engine concern; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the specified cooling system tests and specifications.

__________________________________________________________________

_____  2.  Pressure test the cooling system using a hand-operated pressure tester as per the tester

manufacturer’s instructions.  Results:

____ OK – pressure held						____ NOT OK – pressure dropped					Describe the fault found: ______________________

_____  3.  Pressure test the pressure cap using a hand-operated pressure

tester.

____ OK – pressure held

____  NOT OK

_____  4.  Check the cooling system for presence of combustion gases.  Check the procedure

used.

____  Exhaust gas analyzer checking for HC emissions

____  Coated paper that changes color

____  Liquid tester that changes color

____  Other (describe) _______________________________________________

_____  5.  Results of combustion gas test:

____  Negative (no combustion gases discovered in coolant)

____  Positive (combustion gas discovered in coolant)

_____  6.  Check temperature of cooling system using an infrared pyrometer or other suitable

temperature measuring instrument.

____  Check the radiator for cool areas, which could indicate blockages

____  Compare temperature of the cooling system hoses to thermostat rating

_____  7.  Based on the cooling system tests, what is the needed action? _________________