Crankshaft Inspection

Meets ASE Task:  (A1-C-7) P-1  Inspect crankshaft for straightness, journal damage, keyway

Damage; determine needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check service information for the crankshaft specifications and

inspection procedure.

_______________________________________________

_____  2.  Inspect crankshaft for straightness.    OK ____    NOT OK ____

_____  3.  Check crankshaft journals for damage.		OK ____    NOT OK ____

_____  4.  Check the crankshaft keyway for damage.	OK ____    NOT OK ____

_____  5.  Check the crankshaft thrust flange and sealing surfaces condition.

OK ____    NOT OK ____

_____  6.  Visually check the crankshaft for cracks.		OK ____    NOT OK ____

_____  7.  Measure crankshaft journals and determine if worn.

Main bearing journals:  _____  _____  _____  _____  _____  _____  _____

Rod bearing journals:   _____  _____  _____  _____  _____  _____

_____  8.  Based on the results of the inspection and measurement of the crankshaft, what is the

needed action?

__________________________________________________________________

__________________________________________________________________