Engine Fan Inspection and Testing

Meets ASE Task: (A1-D-8) P-1  Inspect and text fans(s) (electrical or mechanical), fan clutch, fan shroud, and air dams.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Identify the type of cooling fans.

____  Engine driven

____  Electric  (If electric, one or two fans? ____)

____  Hydraulically operated

_____  2.  If mechanical, check the fan clutch for fluid (silicone

fluid) leakage or other damage.

OK _____    NOT OK _____  Describe the fault: _________________________

_____  3.  Check the mechanical fan clutch for proper operation by placing cardboard over the

front of the radiator and start the engine.  Allow the engine to reach normal operating

temperature.  As the temperature of the coolant increases above the normal

temperature range, the fan noise should increase indicating that the fan clutch has

engaged.

OK _____    NOT OK _____

_____  4.  Inspect the fan shroud for damage or if the shroud is missing.

OK _____    NOT OK _____

_____  5.  Inspect that the air dam underneath the front of the vehicle is in place and not missing

or damaged.

OK _____    NOT OK _____

_____  6.  From the inspection above, what is the needed action?  _________________________

_____________________________________________________________________