Radiator Testing with an Infrared Pyrometer

Meets NATEF Task:  (A1-D-3)  Perform cooling system pressure tests; check coolant condition; inspect and test radiator, pressure cap, coolant recovery tank, and hoses.  (P-1)

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check to see if an infrared pyrometer can be aimed to most areas of the radiator from

the engine side.

NOTE:  The fan(s) shroud may have to be removed to gain access.

_____  2.  What had to be removed to allow access? ___________________________________

_____________________________________________________________________

_____  3.  Start the engine and operate until normal operating temperature is achieved and the

thermostat is fully open.

_____  4.  Using an infrared pyrometer, measure the radiator at the inlet, middle, and outlet

sections and record the readings.

Inlet 	=  __________ (should be the hottest)

Middle =  __________ (should be cooler than the inlet section)

Outlet  =  __________ (should be cooler than the middle)

OK _____	NOT OK _____

_____  5.  Aim the infrared pyrometer to all sections of the radiator and look for any areas that

are cooler than the surroundings which indicate a restricted or clogged portion of the

radiator.

OK _____	NOT OK _____

_____  6.  Reinstall any shrouds removed to gain access to the radiator.

_____  7.  Based on the inspection and temperature tests, what is the necessary action?

__________________________________________________________________

__________________________________________________________________