Pre-Alignment Inspection

Meets ASE Task:  (A4-E-2) P-1  Perform prealignment inspection and measure vehicle ride height; perform needed action.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

_____  1.  Check tires.  Both front tires and both

rear tires should be checked for the

following:

A.  Correct tire pressure

B.  Same size and brand

C.  Same tread depth

OK _____     NOT OK _____

_____  2.  Perform a dry-park test to check for any looseness in the steering and suspension

components such as:

A.  Tie rods

B.  Idler arms

C.  Ball-joints

D.  Control arm bushings

E.  Loose or defective wheel bearings

OK _____     NOT OK _____

_____  3.  Check for proper ride height.

A.  Front and rear

B.  Left and right

OK _____     NOT OK _____