Air-Conditioning System Performance Test

Meets ASE Task:  (A7-A-3) P-1  Performance test the A/C system and diagnose using principles of refrigeration.

Name _______________________________   Date ___________  Time on Task __________

Make/Model/Year _________________   VIN ________________   Evaluation:   4    3    2    1

NOTE:  This test procedure is best performed when the temperature is above 70( F (21( C).

_____  1.  Start the engine, turn the air conditioning to maximum cooling, open the doors and

windows, and increase engine speed to about 1500-2000 RPM.

_____  2.  Turn the blower motor to high speed.

_____  3.  Measure the temperature of the air at the air-conditioning vent in the center of the

dash.

Temperature = ______  [should be 35( - 45( F (2( - 7( C)]

OK_____		NOT OK_____

_____  4.  Record high-side and low-side pressures  _______________   ________________

_____  5.  Stop the engine and visually inspect the condition of the air-conditioning compressor

drive belt (accessory drive belt).

OK_____		NOT OK_____

_____  6.  Visually check for any signs of leaking refrigerant oil that could indicate a refrigerant

leak.

OK_____		NOT OK_____