## Slide 1: Automotive Technology: Principles, Diagnosis, and Service
Seventh Edition
Chapter 1
Automotive Background and Overview
Copyright © 2023 Pearson Education, Inc. All Rights Reserved
Notes: INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
1.1 Explain the evolution of the automobile.
1.2 Discuss the components of the vehicle body, frame, and chassis.
1.3 Describe the evolution of engines.
1.4 Describe the purpose of the powertrain.
1.5 List the major systems common to most vehicles.
1.6 Provide an overview of the electrical/electronic systems.
1.7 Provide an overview of the heating, ventilation, and air-conditioning systems.

## Slide 3: Historical Background
Self-propelled vehicles—vehicles that move under their own power
Developed after the invention of electric, steam,
and gasoline propulsion systems
Replace walking and animal use

## Slide 4: Figure 1.1
A model of the Quadricycle, a car built by Henry Ford in 1896

## Slide 5: Bodies, Chassis Systems, & Frames
Early motor vehicles evolved from horse-drawn carriages.
Most vehicle bodies were constructed with a
Wood framework until the 1920s.

## Slide 6: Chassis Systems Overview
Chassis system of the vehicle includes:
  Frame or body
  Suspension system
  Braking system
  Wheels and tires
Notes: Instructor Notes
The chassis system of the vehicle includes the following components:
Frame or body of the vehicle, which is used to provide the support for the suspension and steering components as well as the powertrain.
The suspension system of the vehicle provides a smooth ride to the driver and passengers and helps the tires remain on the road even when the vehicle is traveling over rough roads. The suspension system includes springs and control arms that allow the wheel to move up and down and
keep the tires on the road.
The braking system of the vehicle is used to slow and stop the rotation of the wheels, which in turn stops the vehicle. The braking system includes the brake pedal, master cylinder, plus wheel brakes at each wheel. Two types of wheel brakes are used. Disc brakes include a caliper, which applies force to brake pads on both sides of a rotating disc or rotor. Drum brakes use brake shoes,
which are applied by hydraulic pressure outward against a rotating brake drum. The brake drum is attached to and stops the rotation of the wheels. Drum brakes are used on the rear of many vehicles.
Wheels and tires—The wheels are attached to the bearing hubs on the axles. The tires must provide traction for accelerating, braking, and cornering, as well as provide a comfortable ride. Wheels are constructed of steel or aluminum alloy and mount to the hubs of the vehicle using
lug nuts, which must be tightened correctly to the proper torque.

## Slide 7: Figure 1.2 Wood Body
Most vehicle bodies were constructed with a wood framework until the 1920s

## Slide 8: Question 1
Early vehicles were constructed mostly of what material?

## Slide 9: Answer 1
Wood.

## Slide 10: Figure 1.3 Vehicle Platforms
Some vehicle manufacturers are able to manufacture one platform that can be used with an internal combustion engine, a plug-in hybrid powertrain, or a full electric powertrain.

## Slide 11: Figure 1.4 Body and Terms
Notes: BODY TERMS The roof of a vehicle is supported by pillars and they are labeled A, B, C, and D from
the front to the rear of the vehicle. All vehicles have an A pillar at the windshield but many,
such as a hardtop, do not have a B pillar. Station wagons and sport utility vehicles (SUVs) often
have a D pillar at the rear of the vehicle. SEE FIGURE 1–4.

## Slide 12: Animation: Body Terms (Animation will automatically start)

## Slide 13: Frames (1 of 3)
Frame Construction
  Vehicles with a separate frame and body
  Called body-on-frame (B O F) vehicles.
Notes: Frame construction usually consists of channel- shaped steel beams welded and/or fastened together. Vehicles with a separate frame and body are usually called body-on- frame (BOF) vehicles. Many terms are used to label or describe of a vehicle including: unit-body construction (sometimes called unibody) is a design that combines the body with the structure of the frame.

## Slide 14: Frames (2 of 3)
Unit–Body Construction
  Combines the body with structure of the frame
  Composed of many individual stamped-steel panels
  Welded together

## Slide 15: Figure 1.5 Vehicle Body
Note the ribbing and the many different pieces of sheet metal used in the construction of this body
Notes: Tech Tip: Treat a Vehicle Body with Respect
Do not sit on a vehicle. The metal can easily be distorted, which could cost hundreds of dollars to repair. This includes sitting on the hood, roof, and deck (trunk) lid, as well as fenders. Also, do
not hang on any opened door as this can distort the hinge area causing the door not to
close properly.

## Slide 16: Frames (3 of 3)
Space-Frame Construction
  Consists of formed sheet steel used to
  Construct a framework of the entire vehicle.
  The vehicle is drivable without the body.
  Plastic or steel panels cover the framework.

## Slide 17: Figure 1.6 Corvette Body
A corvette without the body. Notice that the vehicle is complete enough to be driven. This photo was taken at the Corvette Museum in Bowling Green, Kentucky

## Slide 18: Engine Design Evolution (1 of 2)
Internal Combustion Engine
  All gasoline and diesel engines
  Designed to compress an ignitable mixture
Inline Versus V-Type Design
  Inline: 4 or 6 cylinders arranged inline
  V-Type: 4, 6, 8,10,12, or 16 cylinders arranged
  Half cylinders on each side of “V”
  Connected to common crankshaft

## Slide 19: Engine Design Evolution (2 of 2)
Valve Location Design
  Flathead: Valves located in the engine block
  Overhead valve (O H V): Valves located in head
  Single Overhead Cam (S O H C): Camshaft and valves located in head
  Double Overhead Cam (D O H C): Two camshafts and valves located in head

## Slide 20: Figure 1.7 Flathead V8
A Ford flathead V-8 engine. This engine design was used by Ford from 1932 through 1953. In a flathead design, the valves are located next to (beside) the cylinders

## Slide 21: Question 2:
Why were early engines referred to as flat head design?

## Slide 22: Answer 2
The cylinder head did not contain the valves.

## Slide 23: Frequently Asked Question: What Is the Monroney Label?
What Is the Monroney Label? The Monroney label is the sticker on the vehicle that lists the Manufacturer’s Suggested Retail Price, usually abbreviated MSRP. The law that requires this label on all vehicles is called the Monroney Law, named for the congressman who sponsored the bill, Almer S. Monroney (1902–1980), a U.S. farm representative from Oklahoma from 1939 to 1951 and a U.S. Senator from 1951 to 1969. Before the Monroney label law was passed in 1958, the price of a vehicle was unknown to new vehicle buyers who had to rely on the dealer for pricing. Besides all of the standard and optional equipment on the vehicle, the Monroney label also includes fuel economy and exhaust emission information. Figure 1-8
? Frequently Asked Question

## Slide 24: Figure 1.8 Monroney Label
A Monroney label as shown on the side window of a new vehicle
Notes: What Is the Monroney Label? The Monroney label is the sticker on the vehicle that lists the Manufacturer’s Suggested Retail Price, usually abbreviated MSRP. The law that requires this label on all vehicles is called the Monroney Law, named for the congressman who sponsored the bill, Almer S. Monroney (1902–1980), a U.S. farm representative from Oklahoma from 1939 to 1951 and a U.S. Senator from 1951 to 1969. Before the Monroney label law was passed in 1958, the price of a vehicle was unknown to new vehicle buyers who had to rely on the dealer for pricing. Besides all of the standard and optional equipment on the vehicle, the Monroney label also includes fuel economy and exhaust emission information. Figure 1-8

## Slide 25: Engine Systems Overview (1 of 7)
Cooling System
  Coolant circulated by a water pump through passages in the block called water jackets.
  Coolant is mixture of antifreeze and water to provide corrosion and freeze protection.
  Engine heat removed from coolant when it flows through a radiator.
  Temperature of coolant maintained using a thermostat.

## Slide 26: Engine Systems Overview (2 of 7)
Lubrication System (Continued)
  Forces oil under pressure through engine
  To reduce friction and heat
  Oil pan or oil sump holds the oil
  Oil pump forces the oil under pressure
  Through oil filter and oil galleries
  In block and cylinder head

## Slide 27: Engine Systems Overview (3 of 7)
Air Intake System
  All engines draw air from the atmosphere.
  Approximately 9000 gallons of air is
  Needed for every gallon of fuel.
  The air must be drawn into the engine
  From a place water cannot enter.
  Air is filtered by a replaceable air filter.
  Filtered air passes through the throttle valve
  Into the intake manifold.

## Slide 28: Engine Systems Overview (4 of 7)
Fuel System
  Fuel system includes following components & systems:
    Fuel tank
    Fuel lines and filter(s)
    Fuel injectors
    Electronic control of the fuel pump and fuel injection

## Slide 29: Engine Systems Overview (5 of 7)
Starting and Charging System
  Includes the following components:
    Battery
    Starter
    Alternator
    Associated circuits

## Slide 30: Engine Systems Overview (6 of 7)
Ignition System
  Ignition Coils
    Create a high voltage spark
  Ignition Control Module
    Controls the timing of the spark

## Slide 31: Engine Systems Overview (7 of 7)
Emission Control System
  Control of tailpipe and evaporative emissions
  Using the following systems:
    Positive Crankcase Ventilation (P C V)
    Exhaust Gas Recirculation (E G R)
    Catalytic converter
    On-board diagnostics

## Slide 32: Powertrain Overview (1 of 3)
Rear-Wheel-Drive Powertrain
  Transmission: an automatic/manual method of providing the correct torque for the desired speed.
  Driveshaft (also called a propeller shaft):
  Used to connect the transmission to the differential.
  Differential: allows for different axle speeds
  For cornering and increase torque to the drive wheels.

## Slide 33: Powertrain Overview (2 of 3)
Front-Wheel-Drive Powertrain
  Uses transaxle
    Combination of transmission & differential in one assembly.
    Drive axle shafts transfer power to front drive wheels.

## Slide 34: Powertrain Overview (3 of 3)
Four-Wheel-Drive System
  Powers all four wheels
  Many systems
    A transfer case splits engine torque to both front and rear wheels.

## Slide 35: Figure 1.9
A dash control panel used by the driver to control the four-wheel-drive system

## Slide 36: Electrical/Electronic Systems Overview
Systems include:
  Tire pressure monitoring
  Heated and cooled seats
  Automatic climate control
  Power windows
  Security systems
  Electric power steering
  Electronic suspension
Notes: NOTE on Air Conditioning: Today, air-conditioning systems are on most vehicles and
incorporate defrosters and passenger compartment heating, often in two zones for maximum comfort of
the driver and passenger. Additional related comfort options today include heated
and cooled seats, and heated steering wheels.

## Slide 37: Figure 1.10
The alternator is responsible for supplying the electrical needs of the vehicle and to keep the battery charged

## Slide 38: Animation: World Car Production (Animation will automatically start)

## Slide 39: Question 3: ?
What component regulates the temperature of the coolant in an engine?
  a. Cooling (water) jackets
  b. Thermostat
  c. Cooling fan(s)
  d. Radiator

## Slide 40: Answer 3
What component regulates the temperature of the coolant in an engine?
  b. Thermostat

## Slide 41: Automotive Fundamentals Videos and Animations
Videos Link: (A0) Automotive Fundamentals Videos
Animations Link: (A0) Automotive Fundamentals Animations

## Slide 42: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.