## Slide 1: Automotive Technology: Principles, Diagnosis, and Service
Seventh Edition
Chapter 5
Shop Safety
Copyright © 2023 Pearson Education, Inc. All Rights Reserved
Notes: INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
5.1 Describe the personal protective equipment (P P E) technicians use.
5.2 Explain safety tips for automotive technicians.
5.3 Discuss electrical cord safety, jump-starting, and battery safety.
5.4 Discuss the purpose of fire extinguishers and fire blankets.
5.5 Discuss the purpose of first aid and eye wash stations
5.6 Discuss the purpose of evacuation routes.

## Slide 3: Personal Protective Equipment (1 of 4)
Safety Glasses
  Wear at all times
  A N S I Z87.1standard
  Full face shied recommended when using grinder or power washer

## Slide 4: Figure 5.1 Safety Glasses
Safety glasses should be worn at all times when working on or around any vehicle or servicing any component

## Slide 5: Personal Protective Equipment (2 of 4)
Steel-Toed Shoes
  Good investment
  Safer than canvas or cloth

## Slide 6: Figure 5.2 Steel Toes Shoes
Figure 5.2 Steel-toed shoes are a worthwhile investment to help prevent foot injury due to falling objects

## Slide 7: Personal Protective Equipment (3 of 4)
Gloves
  Latex
  Vinyl
  Polyurethane
  Nitrile
  Mechanics

## Slide 8: Figure 5.3 Protective Gloves
Protective gloves, such as these vinyl gloves, are available in several sizes. Select the size that allows the gloves to fit snugly. Vinyl gloves last a long time and often can be worn all day to help protect your hands from dirt and possible hazardous materials

## Slide 9: Personal Protective Equipment (4 of 4)
Bump Cap
  Protects head when working under vehicle.
Hands, Jewellery, Clothing
  Remove jewellery and keep hands clean.
Hearing Protection
  Used when noise is greater than 90 dB

## Slide 10: Figure 5.4 Bump Cap
Figure 5.4 One version of a bump cap is this padded plastic insert that is worn inside a regular cloth cap

## Slide 11: Figure 5.5 Hearing Protection
Figure 5.5 Hearing protection is recommended for use if the noise level exceeds 90 dB, which is often the case in a noisy automotive shop if air tools or grinders are being used
Notes: TECH TIP: Professional Behavior in the Shop Is a Must To be respected as a professional service technician and for safety, always behave in a professional manner. These behaviors include, but are not limited to, the following:
■ Show respect to other technicians and employees. For example, the shop owner or service manager may not always be right, but they are always the boss.
■ Avoid horseplay or practical jokes.
■ Act as if a customer is observing your behavior at all times because this is often the case.

## Slide 12: Question 1
What are the four items that are personal protective equipment?

## Slide 13: Answer 1
Safety glasses, steel-toed boots, bump cap, and gloves.

## Slide 14: Safety Tips for Technicians (1 of 2)
Lifting
  Secure grip and solid footing
  Do not twist
  Ask for help
  Push rather than pull
Exhaust Hose
  Make sure it is properly connected to vehicle

## Slide 15: Figure 5.6 Exhaust Venting
Figure 5.6 Always connect an exhaust hose to the tailpipe of the engine of a vehicle to be run inside a building

## Slide 16: Safety Tips for Technicians (2 of 2)
Work Height
  Place tools nearby to avoid strain
Hood
  Ensure it is securely open
Moving Vehicles
  Get help or used motorized pusher

## Slide 17: Figure 5.7 Lifting Heavy Objects
When lifting heavy objects, lift using your legs instead of your back to help avoid strain and injury.

## Slide 18: Figure 5.8 Electric Pusher
Figure 5.8 An electric pusher used to push vehicles into or around the shop

## Slide 19: Figure 5.9 Rag Container
All oily shop cloths should be stored in a metal container equipped with a lid to help prevent spontaneous combustion
Notes: SAFETY TIP: Shop Cloth Disposal: Always dispose of oily shop cloths in an enclosed container to prevent a fire. ● SEE FIGURE 5–9. Whenever oily cloths are thrown together on the floor or workbench, a chemical reaction can occur which can ignite the cloth even without an open flame. This process of ignition without an open flame is called spontaneous combustion.

## Slide 20: Animation: Spontaneous Combustion (Animation will automatically start)

## Slide 21: Electrical Safety
Electrical Cord Safety
  Use three-prong grounded outlets and cords.
Jump Starting and Battery Safety
  Use quality jumper cables or jumper box.
  The last connection should be on the block away from the battery.

## Slide 22: Figure 5.10 Jumper cable usage guide

## Slide 23: Animation: Jumper Cable Usage (Animation will automatically start)

## Slide 24: Animation: Jumper Box Cable Usage (Animation will automatically start)

## Slide 25: Animation: Jumper Starting Hybrid (Animation will automatically start)

## Slide 26: Figure 5.11 Pressure Gauge
The air pressure going to the nozzle should be reduced to 30 P S I or less
Notes: SAFETY TIP: Compressed Air Safety
Improper use of an air nozzle can cause blindness or deafness. Compressed air must be reduced to
less than 30 PSI (206 kPa). ● SEE FIGURE 5–11. If an air nozzle is used to dry and clean parts,
make sure the air stream is directed away from anyone else in the immediate area. Always use an
OSHA-approved nozzle with side slits that limit the maximum pressure at the nozzle to 30 PSI. Coil
and store air hoses when they are not in use.

## Slide 27: Fire Safety (1 of 3)
Fire Extinguishers
  Class A is designed for use on general combustibles, such as cloth, paper, and wood.
  Class B is designed for use on flammable liquids and greases, including gasoline, oil, thinners, and solvents.
  Class C is used only on electrical fires.
  Class D is effective only on combustible metals, such as powdered Aluminium, sodium, or magnesium.

## Slide 28: Figure 5.12 Fire Extinguisher
Figure 5.12 A typical fire extinguisher designed to be used on type class A, B, or C fires. The area around the fire extinguisher must be free and clear to allow easy access

## Slide 29: Fire Safety (2 of 3)
Types of Fire Extinguishers
  Water
    Reduces temperature where fire cannot be sustained
  Carbon Dioxide (C O 2)
    Removes oxygen from the fire and reduces the temperature
  Dry Chemical (Yellow)
    Coats the flammable material which eliminates the oxygen from the fire

## Slide 30: Figure 5.13 Putting Out Fire
A CO2 fire extinguisher being used on a fire set in an open steel drum during a demonstration at a fire department training center

## Slide 31: Fire Safety (3 of 3)
Fire Blankets
  Used when a person is on fire
  Smothers the flames
First Aid and Eye Wash Stations
  First aid station contains emergency supplies
  Eye wash station used to rinse liquids or chemicals
Evacuation Routes
  Easy to read instructions on how to exit in an emergency

## Slide 32: Figure 5.14 Fire Blanket
A treated wool blanket is kept in this easy-to-open wall-mounted holder and should be placed in a centralized location in the shop

## Slide 33: Figure 5.15 First Aid Box
A first aid box should be centrally located in the shop and kept stocked with the recommended supplies

## Slide 34: Figure 5.16 Typical Eye Wash Station
A typical eye wash station. Often a thorough flushing of the eyes with water is the best treatment in the event of eye contamination

## Slide 35: Figure 5.17 Evacuation Routes
The evacuation routes from where you are in the building is shown on maps that are attached to the walls in schools and commercial buildings

## Slide 36: Animation: Evacuation Routes (Animation will automatically start)

## Slide 37: Figure 5.18 Properly Marked Aisle
A properly marked aisle using yellow paint stripes leading to an exit
Notes: SAFETY TIP: Infection Control Precautions
Working on a vehicle can result in personal injury including the possibility of being cut or hurt enough to cause bleeding. Some infections such as hepatitis B, HIV (which can cause acquired immunodeficiency syndrome, or AIDS), and hepatitis C virus are transmitted through blood. These infections are commonly called blood-borne pathogens. Report any injury that involves blood to your supervisor and take the necessary precautions to avoid coming in contact with blood from another person.

## Slide 38: Question 2
What are the three types of fire extinguishers?

## Slide 39: Answer 2
Water, carbon dioxide, and dry chemical.

## Slide 40: Automotive Fundamentals Videos and Animations
Videos Link: (A0) Automotive Fundamentals Videos
Animations Link: (A0) Automotive Fundamentals Animations

## Slide 41: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.