## Slide 1: Automotive Technology: Principles, Diagnosis, and Service
Seventh Edition
Chapter 44
Magnetism and Electromagnetism
Copyright © 2023 Pearson Education, Inc. All Rights Reserved
Notes: INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
44.1 Define magnetism and explain the concepts of magnetic induction, permeability, and reluctance.
44.2 Explain how an electromagnet works.
44.3 Explain how electromagnetism is used in relays and solenoids.
44.4 Discuss electromagnetic induction.
44.5 Describe how an ignition coil works.
44.6 Describe ways to reduce electromagnetic interference.

## Slide 3: Fundamentals of Magnetism (1 of 4)
Definition
  Magnetism is form of energy that is caused by the motion of electrons in some materials.
  Like electricity, magnetism cannot be seen.
  Magnetite is the most naturally occurring magnet.
  Many other materials can be artificially magnetized to some degree, depending on their atomic structure.

## Slide 4: Fundamentals of Magnetism (2 of 4)
Lines of Force
  The lines that create a field of force around a magnet are believed to be caused by the way groups of atoms are aligned in the magnetic material.
Magnetic Induction
  If a piece of iron or steel is placed in a magnetic field, it also becomes magnetized.

## Slide 5: Fundamentals of Magnetism (3 of 4)
Attracting or Repelling
  When unlike poles are placed close together, the lines exit from one magnet and enter the other.
  If like poles are placed close together, the curving flux lines meet head-on, forcing the magnets apart.

## Slide 6: Fundamentals of Magnetism (4 of 4)
Permeability
  The degree that some materials allow the magnetic force to pass through more easily than others.
Reluctance
  The degree that certain materials resist the passage of magnetic force.

## Slide 7: Figure 44.1 Loadstone
A Freely Suspended Natural Magnet (Lodestone) Points Toward the Magnetic North Pole

## Slide 8: Figure 44.2 Magnet Breaks
If a Magnet Breaks or Is Cracked, It Becomes Two Weaker Magnets
Notes: TECH TIP: A Cracked Magnet Becomes Two Magnets
Magnets are commonly used in vehicle crankshaft, camshaft, and wheel speed sensors. If a magnet is struck and cracks or breaks, the result is two smaller-strength magnets. Because the strength of the magnetic field is reduced, the sensor output voltage is also reduced. A typical problem occurs when a magnetic crankshaft sensor becomes cracked, resulting in a no-start condition. Sometimes the cracked sensor works well enough to start an engine that is cranking at normal speeds, but does not work when the engine is cold. See Figure 44-2.

## Slide 9: Figure 44.3 Magnetic Lines of Force
Magnetic Lines of Force Leave the North Pole and Return to the South Pole of a Bar Magnet

## Slide 10: Animation: Magnets (Animation will automatically start)

## Slide 11: Question 1: ?
What is the result if a magnet cracks?

## Slide 12: Answer 1
Two weaker magnets are created.

## Slide 13: Electromagnetism (1 of 3)
Definition
  A current carrying conductor surrounded by a magnetic field, many time stronger than a conventional magnet.
Creating an Electromagnet
  Wrap a nail with 20 turns of insulated wire and connect the ends to the terminals of a 1.5 volt dry cell battery.
Straight Conductor
  The magnetic field surrounding a straight, current-carrying conductor consists of several concentric cylinders of flux that are the length of the wire.

## Slide 14: Electromagnetism (2 of 3)
Left-Hand/Right-Hand Rules
  Left-hand rule for magnetic field direction is used with the electron flow theory.
  Right-hand rule for magnetic field direction is used with the conventional theory of electron flow.
Field Interaction
  Conductors with opposing magnetic fields move apart into weaker fields.
Motor Principle
  Use the magnetic field interaction to convert electrical energy into mechanical energy.

## Slide 15: Electromagnetism (3 of 3)
Coil Conductor
  If several loops of wire are made into a coil, then the magnetic flux density is strengthened.
Electromagnetic Strength
  The magnetic field can be strengthened (increased) in three ways.
    Place a soft iron core in the center of the coil.
    Increase the number of turns of wire in the coil.
    Increase the current flow through the coil windings.

## Slide 16: Figure 44.4 Iron Fillings/Compass
Iron Filings and a Compass Can Be Used to Observe the Magnetic Lines of Force

## Slide 17: Figure 44.5 Magnetic Poles
(a) Magnetic Lines of Force Spread out from Around an Isolated Magnet. (b) Opposite Poles Attract. (c) Similar Poles Repel
Notes: TECH TIP: Magnetize a Steel Needle
A piece of steel can be magnetized by rubbing a magnet in one direction along the steel. This causes the atoms to line up in the steel, so it acts like a magnet. The steel often does not remain magnetized, whereas the true magnet is permanently magnetized. When soft iron or steel is used, such as a paper clip, it loses its magnetism quickly. The atoms in a magnetized needle can be disturbed by heating it or by dropping the needle on a hard object, which causes the needle to lose its magnetism. Soft iron is used inside ignition coils because it does not keep its magnetism.

## Slide 18: Figure 44.6 Reluctor Wheel
A Crankshaft Position Sensor and Reluctor (Notched Wheel)

## Slide 19: Figure 44.7 Magnetic Field
A Magnetic Field Surrounds a Straight, Current-Carrying Conductor

## Slide 20: Figure 44.8 Left-Hand Rule
The Left-Hand Rule for Magnetic Field Direction Is Used with the Electron Flow Theory

## Slide 21: Figure 44.9 Right-Hand Rule
47.9 The Right-Hand Rule for Magnetic Field Direction Is Used with the Conventional Theory of Electron Flow

## Slide 22: Figure 44.10 Opposing Fields
Conductors with Opposing Magnetic Fields Move Apart into Weaker Fields
Notes: TECH TIP: Electricity and Magnetism
Electricity and magnetism are closely related because any electrical current flowing through a
conductor creates a magnetic field. Any conductor moving through a magnetic field creates an
electrical current. This relationship can be summarized as follows:
• Electricity creates magnetism.
• Magnetism creates electricity.
From a service technician’s point of view, this relationship is important because wires carrying
current should always be routed as the factory intended to avoid causing interference with another
circuit or electronic component. This is especially important when installing or servicing spark
plug wires, which carry high voltages and can cause high
electromagnetic interference.

## Slide 23: Figure 44.11 Motor Fields
Electric Motors Use the Interaction of Magnetic Fields to Produce Mechanical Energy

## Slide 24: Animation: DC Motor, Simple (Animation will automatically start)

## Slide 25: Figure 44.12 Coil Flux
The Magnetic Lines of Flux Surrounding a Coil Look like Those Surrounding a Bar Magnet

## Slide 26: Figure 44.13 Left-Hand Rule
The Left-Hand Rule for Coils Is Shown

## Slide 27: Figure 44.14 Iron Core Flux
An Iron Core Concentrates the Magnetic Lines of Force Surrounding a Coil

## Slide 28: Use of Electromagnetism
Relays
  A simple relay contains an electromagnetic coil in series with a battery and a switch.
Solenoid
  A solenoid is an example of an electromagnetic switch that uses a moveable core.

## Slide 29: Figure 44.15 Relay
An Electromagnetic Switch That Has a Movable Arm Is Referred to as a Relay

## Slide 30: Animation: Relay (Animation will automatically start)

## Slide 31: Frequently Asked Question: Solenoid or Relay?
Solenoid or Relay? Often, either term is used to describe the same part in service information. ● SEE CHART 44–1 for a summary of the differences.
? Frequently Asked Question

## Slide 32: Chart 44.1 Relay Solenoid Comparison
 | Construction | Amperage | Uses | Service info
Relay | Uses a movable arm: Coil: 60–100 ohms requiring 0.12–0.20 ampere to energize | 1-30 amps | Lower current switching, lower cost, more commonly used | Electromagnetic switch or relay
Solenoid | Uses a movable core. Coil(s): 0.2–0.6 ohm requiring 20–60 amperes to energize | 30-400 amps | Higher cost, used in starter motor circuits and other high-amperage applications | Solenoid, relay, or electromagnetic switch
Chart 44-1 Comparison between a relay and a solenoid

## Slide 33: Animation: Normally Closed Solenoid (Animation will automatically start)

## Slide 34: Figure 44.16 Starter Armature
(a) A starter with attached solenoid. All the current needed by the starter flows through the two large terminals of the solenoid and through the solenoid contacts inside. (b) A relay is designed to carry lower current, compared to a solenoid, and uses a movable arm.

## Slide 35: Electromagnetic Induction (1 of 2)
Principles Involved
  Electricity can be produced by using the relative movement of an electrical conductor and a magnetic field.
Voltage Intensity
  The amount of the voltage depends on the rate at which the flux lines are broken.
Lenz’s Law
  An induced current moves so that its magnetic field opposes the motion that induced the current.

## Slide 36: Electromagnetic Induction (2 of 2)
Self-Induction
  As current increases, the flux lines continue to expand, cutting across the wires of the coil and actually inducing another voltage within the same coil.
Mutual Induction
  When two coils are close together, energy may be transferred from one to the other by magnetic coupling.

## Slide 37: Figure 44.17 Magnetic Flux Lines
Voltage Can Be Induced by the Relative Motion Between a Conductor and Magnetic Lines of Force

## Slide 38: Figure 44.18 Cutting Lines of Force
Maximum Voltage Is Induced When Conductors Cut Across the Magnetic Lines of Force (Flux Lines) at a 90-Degree Angle

## Slide 39: Animation: Electron Travel, Magnet (Animation will automatically start)

## Slide 40: Animation: Magnetic Induction (Animation will automatically start)

## Slide 41: Question 2: ?
What is the difference between mutual induction and self-induction?

## Slide 42: Answer 2
In mutual induction there are two coils, in self-induction there is a single coil.

## Slide 43: Ignition Coils
Ignition Coil Windings
  Ignition coils use two windings and are wound on the same iron core.
Ignition Coil Construction
  A core of laminated soft iron is surrounded by the secondary windings. The secondary windings are surrounded by the primary windings.
Ignition Coil Operation
  The coil is fed battery voltage when the key is on and the ground is controlled by an ignition module.

## Slide 44: Figure 44.19 Mutual Inductance
Mutual induction occurs when the expansion or collapse of a magnetic field around one coil induces a voltage in a second coil.

## Slide 45: Figure 44.20 Married Coil
Some Ignition Coils Are Electrically Connected, Called “Married” (Left Figure), Whereas Others Use Separated Primary and Secondary Windings, Called “Divorced” (Right Figure)

## Slide 46: Figure 44.21 GM Waste-Spark Coil
A G M Waste-Spark Ignition Coil Showing the Section of Laminations That Is Shaped like the Letter E. These Mild Steel Laminations Improve the Efficiency of the Coil

## Slide 47: Animation: Waste Spark Ignition System (Animation will automatically start)
Waste Spark Ignition System

## Slide 48: Figure 44.22 COP
The Coil-on-Plug (C O P) Design Typically Uses a Bobbin-Type Coil

## Slide 49: Animation: Coil-On-Plug Ignition System (Animation will automatically start)

## Slide 50: Electromagnetic Interference
Definition
  Electrical interference caused by radio frequency or electromagnetic fields.
How is E M I Created
  When the current in a conductor is turned on/off fast enough, a high-frequency signal wave is created.
E M I Suppression Devices
  Capacitors, coils, shielding, and ground wires or cables

## Slide 51: Figure 44.23 Grounded Wires
To Help Prevent Underhood Electromagnetic Devices from Interfering with the Antenna Input, It Is Important That All Ground Wires, Including the One from This Power Antenna, Be Properly Grounded

## Slide 52: Question 3: ?
How can E M I be reduced or controlled?

## Slide 53: Answer 3
Capacitors, coils, shielding, and ground wires or cables.

## Slide 54: Electrical and Electronic Systems Videos and Animations
Videos Link: (A6) Electrical/Electronic Systems Videos
Animations Link: (A6) Electrical/Electronic Systems Animations

## Slide 55: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.