## Slide 1: Automotive Technology: Principles, Diagnosis, and Service
Seventh Edition
Chapter 51
Charging Systems Parts and Operation
Copyright © 2023 Pearson Education, Inc. All Rights Reserved
Notes: INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives (1 of 2)
51.1 Explain why an alternator generates an A C and changes it to D C.
51.2 Describe an alternator’s construction, including overrunning pulleys.
51.3 Describe the components and operation of an alternator.
51.4 Discuss how an alternator works.

## Slide 3: Learning Objectives (2 of 2)
51.5 List the factors determining an alternator’s output voltage and current.
51.6 Explain how the voltage of an alternator is regulated.
51.7 Explain how the heat produced by an alternator is regulated.
51.8 Discuss computer-controlled alternators.

## Slide 4: Principle of Alternator Operation
Terminology
  S A E term for unit that generates electricity is generator.
  Alternator is most commonly used
Amount of current generated can be increased by:
  Increasing speed of conductors through magnetic field
  Increasing number of conductors passing through magnetic field
  Increasing strength of magnetic field

## Slide 5: Alternator Construction
Housing
  An alternator is constructed using a two-piece cast aluminum housing
  A front ball bearing is pressed into the front housing, called the drive-end (D E) housing
  The rear housing, or the slip-ring-end (S R E) housing, usually contains either a roller bearing or ball bearing

## Slide 6: Question 1: ?
How can the amount of current an alternator generates increase?

## Slide 7: Answer 1
Increase the speed of the conductors, increase the number of conductors, increase the strength of the magnetic field.

## Slide 8: Alternator Overrunning Pulleys
Purpose and Function
  The purpose of this pulley is to help eliminate noise and vibration in the accessory drive belt system.
  May use a dampener spring inside, plus a one-way clutch.
Manufacturer Specific System Names
  Isolating Decoupler Pulley (I D P)
  Active Alternator Pulley (A A P)
  Alternator Decoupler Pulley (A D P)
  Alternator Overrunning Decoupler Pulley

## Slide 9: Figure 51.1 Alternator
A typical alternator on a Chevrolet V-8 engine that is driven by the accessory drive belt at the front of the engine
Notes: TECH TIP: Alternator Horsepower and Engine Operation
Many technicians are asked how much power certain accessories require. A 100 ampere alternator requires about 2 horsepower from the engine.
One horsepower is equal to 746 watts. Watts are calculated by multiplying amperes times volts.
Power in watts = 100 A × 14.5 V = 1, 450 W 1 hp = 746 W
Therefore, 1, 450 watts is about 2 horsepower.
Allowing about 20% for mechanical and electrical losses adds another 0.4 horsepower. Therefore, when someone asks how much power it takes to produce
100 amperes from an alternator, the answer is
  2.4 horsepower.
Many alternators delay the electrical load to prevent the engine from stumbling when a heavy electrical load is applied. The voltage regulator or vehicle computer is capable of gradually increasing the output of the alternator over a period of several
minutes. Even though 2 horsepower does not sound like much, a sudden demand for 2 horsepower
from an idling engine can cause the engine to run rough or stall. The difference in part numbers of various alternators is often an indication of the time interval over which the load is applied. Therefore, using the wrong replacement alternator could cause
the engine to stall!

## Slide 10: Figure 51.2 Frame
The end frame toward the drive belt is called the drive-end housing and the rear section is called the slip-ring-end housing

## Slide 11: Figure 51.3 OAP
An OAP on a Chevrolet Corvette alternator

## Slide 12: Figure 54.4

## Slide 13: Figure 51.4 OAP Exploded View
An exploded view of an overrunning alternator pulley showing all of the internal parts

## Slide 14: Figure 51.5 OAD
An overrunning alternator damper (OAD) is not a simple one-way clutch or a solid pulley, but instead is engineered to dampen noises and vibrations in the front accessory drive belt system

## Slide 15: Frequently Asked Question: Can I Install an OAP or an OAD to My Alternator?
Can I Install an OAP or an OAD to My Alternator? Usually, no. An alternator needs to be equipped with the proper shaft to allow the installation of an OAP or OAD. This also means that a conventional pulley often cannot be used to replace a defective overrunning alternator pulley or dampener. Check service information for the exact procedure to follow.
? Frequently Asked Question

## Slide 16: Question 2: ?
What is the purpose of an O A P or O A D?

## Slide 17: Answer 2
Reduce noise and vibration.

## Slide 18: Alternator Components and Operation (1 of 2)
Rotor Construction
  Rotor constructed of many turns of copper wire coated with a varnish insulation wound over an iron core.
How Rotors Create Magnetic Fields
  Current through slip rings causes “fingers” of rotor to become alternating north and south magnetic poles.

## Slide 19: Alternator Components and Operation (2 of 2)
Rotor Current
  Maximum rated alternator output in amperes depends on the number and gauge of the rotor windings.
Stator Construction
  Stator consists of stationary coil windings inside alternator.
Diodes
  Semiconductor that operate as a one-way electrical check valve.

## Slide 20: Figure 51.6 Cutaway
A cutaway of an alternator, showing the rotor and cooling fan that is used to force air through the unit to remove the heat created when it is charging the battery and supplying electrical power for the vehicle

## Slide 21: Figure 51.7 Rotor Flux
Rotor assembly of a typical alternator. Current through the slip rings causes the “fingers” of the rotor to become alternating north and south magnetic poles. As the rotor revolves, these magnetic lines of force induce a current in the stator windings

## Slide 22: Figure 51.8 Exploded View
An exploded view of a typical alternator showing all of its internal parts, including the stator windings

## Slide 23: Figure 51.9 Rectifier
A rectifier usually includes six diodes in one assembly and is used to rectify A C voltage from the stator windings into DC voltage suitable for use by the battery and electrical devices in the vehicle

## Slide 24: How an Alternator Works (1 of 2)
Field Current Is Produced
  Magnetic field of rotor generates a current in stator windings by electromagnetic induction.
Current Induced in Stator
  Induced current in stator windings is alternating current because of alternating magnetic field of rotor.

## Slide 25: How an Alternator Works (2 of 2)
Wye-Connected Stators
  Wye-type stator connection, the currents must combine because 2 windings are always connected in series.
Delta-Connected Stators
  Current induced in each winding flows to diodes in a parallel circuit.

## Slide 26: Figure 51.10 Magnetic Line of Force
Magnetic lines of force cutting across a conductor induce a voltage and current in the conductor

## Slide 27: Animation: Alternating Current (Animation will automatically start)

## Slide 28: Figure 51.11 Sine Wave
A sine wave (shaped like the letter S on its side) voltage curve is created by one revolution of a winding as it rotates in a magnetic field

## Slide 29: Figure 51.12 Three Windings Wave
54.12 When 3 windings (A, B, and C) present in a stator, the resulting current generation is represented by 3 sine waves. The voltages are 120 degrees out of phase. The connection of the individual phases produces a three-phase alternating voltage

## Slide 30: Figure 51.13 Wye Stator
Wye-connected stator winding

## Slide 31: Figure 51.14 Wye Stator Operation
As magnetic field, created in the rotor, cuts across windings of stator, a current is induced. Notice that current path includes passing through one positive (+) diode on way to battery and one negative (-) diode as a complete circuit is completed through rectifier and stator. It is the flow of current through diodes that converts the AC voltage produced in the stator windings to DC voltage available at the output terminal of the alternator

## Slide 32: Figure 51.15 Delta Wound
Delta-connected stator winding

## Slide 33: Animation: Three Connector Alternator (Animation will automatically start)

## Slide 34: Alternator Output Factors
The output voltage and current of an alternator depend on the following factors.
  Speed of rotation
  Number of conductors
  Strength of the magnetic field

## Slide 35: Figure 51.16 Stator Windings
A stator assembly with 6, rather than normal 3 , windings

## Slide 36: Alternator Voltage Regulation
Regulator Operation
  Control of field current accomplished by opening and closing ground side of field circuit through rotor on most alternators.
  Zener diode is a major electronic component that makes voltage regulation possible.
Battery Condition and Charging Voltage
  The alternator may supply the needed current but may not reach maximum charging voltage.
Voltage regulators compensate for temperature.

## Slide 37: Figure 51.17 Voltage Regulator
Typical voltage regulator range

## Slide 38: Figure 51.18 Electronic Regulator
A typical electronic voltage regulator with the cover removed showing the circuits inside

## Slide 39: Figure 51.19 GM SI Regulator
Typical GM SI-style alternator with an integral voltage regulator. Voltage present at terminal 2 is used to reverse bias the Zener diode (D2) that controls TR2. The positive brush is fed by the ignition current (terminal 1) plus current from the diode trio

## Slide 40: Alternator Cooling
The types of cooling include the following:
  External fan
  Internal fan(s)
  Both an external fan and an internal fan
  Coolant cooled

## Slide 41: Figure 51.20 Coolant Cooled
A coolant-cooled alternator showing the hose connections where coolant from the engine flows through the rear frame of the alternator

## Slide 42: Question 3: ?
How can an alternator be cooled?

## Slide 43: Answer 3
How can an alternator be cooled?

## Slide 44: Computer-Controlled Alternators
Computers can interface with charging system in 3 ways.
  Computer can activate charging system by turning on and off field current to rotor.
  Computer can monitor operation of alternator and increase engine speed.
  Computer can control alternator by controlling alternator output to match needs of system.

## Slide 45: Figure 51.21 Hall-Effect Sensor
A Hall-effect current sensor attached to positive battery cable is used as part of the EPM system

## Slide 46: Figure 51.22 Computer Control
The amount of time current is flowing through the field (rotor) determines the alternator output

## Slide 47: Animation: Hall-Effect Sensor (Animation will automatically start)

## Slide 48: Chart 51.1 Output Voltage
COMMAND DUTY CYCLE | ALTERNATOR OUTPUT VOLTAGE
10% | 11.0 V
20% | 11.6 V
30% | 12.1 V
40% | 12.7 V
50% | 13.3 V
60% | 13.8 V
70% | 14.4 V
80% | 14.9 V
90% | 15.5 V
The output voltage is controlled by varying the duty cycle as controlled by the PCM.

## Slide 49: Electrical and Electronic Systems Videos and Animations
Videos Link: (A6) Electrical/Electronic Systems Videos
Animations Link: (A6) Electrical/Electronic Systems Animations

## Slide 50: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.