## Slide 1: Automotive Technology: Principles, Diagnosis, and Service
Seventh Edition
Chapter 85
Strategy Based Diagnosis
Copyright © 2023 Pearson Education, Inc. All Rights Reserved
Notes: INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
85.1 List the steps of the diagnostic process.
85.2 Discuss the types of scan tools that are used to assess vehicle components.
85.3 Explain how to retrieve diagnostic information and how to use DTCs.
85.4 Explain the troubleshooting procedures to follow if a diagnostic trouble code has been set.
85.5 Explain manufacturer's diagnostic routines.
85.6 Discuss completing system repairs, including resetting the PCM and road test (drive cycle).

## Slide 3: 8-Step Diagnostic Procedure (1 of 6)
Step 1 Verify the Problem (Concern)
  Before a minute is spent on diagnosis, be certain that a problem exists.
Step 2 Perform a Thorough Visual Inspection and Basic Tests
  Check for obvious problems (basics, basics, basics).
  Check everything that does and does not work.
  Look for evidence of previous repairs.
  Check oil level and condition.
  Check coolant level and condition.

## Slide 4: Figure 85.1 Funnel Analogy
A funnel is one way to visualize the diagnostic process. The purpose is to narrow the possible causes of a concern until the root cause is determined and corrected

## Slide 5: Animation: 8-Step Diagnostic Procedure (Animation will automatically start)

## Slide 6: Figure 85.2 Circle Visual
Another way to visualize diagnostic process is in a circle.
Notes: Step 1 is to verify the customer concern or problem. If the problem cannot be verified, then the repair cannot be performed
TECH TIP “Original Equipment” Is Not a Four-Letter Word
To many service technicians, an original-equipment part is considered to be only marginal, and to get the really “good stuff” an aftermarket (renewal market) part has to be purchased. However, many problems can be traced to the use of an aftermarket part that has failed early in its service life. Technicians who work at dealerships usually go immediately to an aftermarket part that is observed during a visual inspection. It has been their experience that simply replacing the aftermarket part with the factory original-equipment (OE) part often solves the problem.
Original equipment parts are required to pass quality and durability standards and tests at a level not required of aftermarket parts. The technician should be aware that the presence of a new part does not necessarily mean that the part is good.

## Slide 7: Figure 85.3 Diagnostic Worksheet
A form that the customer should fill out if there is a driveablility concern to help the service technician more quickly find the root cause

## Slide 8: Figure 85.4 Step 2 Visual Check
This is what was found when removing an air filter from a vehicle that had a lack-of-power concern. Obviously, the nuts were deposited by squirrels or some other animal, blocking a lot of the airflow into the engine

## Slide 9: Figure 85.5 Step 2 Using Bright Light
Using a bright light makes seeing where the smoke is coming from easier. In this case, smoke was added to the intake manifold with the inlet blocked with a yellow plastic cap and smoke was seen escaping past a gasket at the idle air control.
Notes: TECH TIP: Smoke Machine Testing Vacuum (air) leaks can cause a variety of driveability problems and are often difficult to locate. One good method is to use a machine that generates a stream of smoke. Connecting the outlet of the smoke machine to the hose that was removed from the vacuum brake booster allows smoke to enter the intake manifold. Any vacuum leaks will be spotted by observing smoke coming out of the leak. SEE FIGURE 85-5.

## Slide 10: Figure 85.6 Spark Tester
A spark tester connected to a spark plug wire or coil output. A typical spark tester fires only if at least 25,000 volts is available from the coil, making a spark tester a useful tool. Do not use one that just lights when a spark is present, because it does not require more than about 2,000 volts to light

## Slide 11: 8-Step Diagnostic Procedure (2 of 6)
Step 3 Retrieve the Diagnostic Trouble Codes (D T Cs)
  If a diagnostic trouble code (D T C) is present in the computer memory, it may be signaled by illuminating a malfunction indicator lamp (M I L), commonly labeled “check engine” or “service engine soon.”

## Slide 12: Figure 85.7 Step 3
Step 3 in the diagnostic process is to retrieve any stored diagnostic trouble codes

## Slide 13: 8-Step Diagnostic Procedure (3 of 6)
Step 4 Check for Technical Service Bulletins
  Check for corrections in technical service bulletins (T S B s) that match the symptoms.
  As many as 30% of vehicles can be repaired following the information, suggestions, or replacement parts found in a service bulletin.

## Slide 14: Figure 85.8 Step 4 Check for TSBs
After checking for stored diagnostic trouble codes (DTCs), technician checks service information for any technical service bulletins (TSBs) that may relate to the vehicle being serviced

## Slide 15: 8-Step Diagnostic Procedure (4 of 6)
Step 5 Look Carefully at Scan Tool Data
  Vehicle manufacturers have been giving the technician more and more data on a scan tool connected to the data link connector (D L C).
  The best way to look at scan data is in a definite sequence and with specific, selected bits of data that can tell the most about the operation of the engine.

## Slide 16: Figure 85.9 Step 5 Scan Tool Data
Looking carefully at the scan tool data is very helpful in locating the source of a problem
Notes: TECH TIP: Look at the Freeze Frame
Whenever a DTC is set, a freeze frame is stored. The freeze frame includes data showing how the engine was being operated at the time the code was set.
The wise service technician saves the freeze frame information to help determine not only what might have caused the code to set but also to allow the technician to drive the vehicle under similar conditions to verify that the problem has been corrected.

## Slide 17: 8-Step Diagnostic Procedure (5 of 6)
Step 6 Narrow the Problem to a System or Cylinder
  Narrowing the focus to a system or individual cylinder is the hardest part of the entire diagnostic process.
  Perform specific tests such as a power balance test, a compression test, or a cylinder leakage test.
Step 7 Repair the Problem and Determine the Root Cause
  The repair or part replacement must be performed following vehicle manufacturer’s recommendations.

## Slide 18: 8-Step Diagnostic Procedure (6 of 6)
Step 8 Verify the Repair and Clear any Stored D T Cs
  Test-drive to verify that the original problem (concern) is fixed.
  Verify that no additional problems have occurred during the repair process.
  Check for and then clear all D T Cs.

## Slide 19: Figure 85.10 Step 8 Verify Repair
Step 8 is very important. Be sure that the customer’s concern has been corrected
Notes: TECH TIP: One Test Is Worth 1,000 “Expert” Opinions
Whenever any vehicle has an engine performance or driveability concern, certain people always say:
“Sounds like it’s a bad injector.”
“I’ll bet you it’s a bad computer.”
“I had a problem just like yours yesterday and it was a bad EGR valve.”
Regardless of the skills and talents of those people, it is still more accurate to perform tests on
the vehicle than to rely on feelings or opinions of others who have not even seen the vehicle. Even
your own opinion should not sway your thinking. Follow a plan, perform
tests, and the test results will lead to the root cause.

## Slide 20: Chart 85.1 Short-Term Fuel Trim
TOTAL FUEL TRIM (LTFT + STFT) AT IDLE | 2,500 RPM FUEL TRIM | LOADED FUEL TRIM | DRIVABILITY SYMPTOMS | POSSIBLE CAUSES
0–5% | 0–5% | 0–5% | No issues | Preferred fuel trim values
6–10% | 6–10% | 6–10% | No issues | Acceptable fuel trim valves
−10+ % | −10+ % | −10+ % | Poor fuel economy | PCM is reducing fuel do to faults in the fuel system over-fueling the engine
+10%+ | +10%+ | +10%+ | Low power, possible hesitation on acceleration | PCM is increasing fuel delivery do to faults in the air induction system
Normal short term fuel trim (STFT and long term fuel trim (LTFT) are considered to be less than +/− 10%.

## Slide 21: Question 1: ?
What is the purpose of the eight-step diagnostic process?

## Slide 22: Answer 1
To ensure the concern is properly identified and fixed correctly on the first visit.

## Slide 23: Scan Tools
Scan tools divided into 2 groups:
  Factory Scan Tools
    Factory scan tools designed to provide bidirectional capability
    Factory scan tools capable of displaying all factory parameters.
  Aftermarket Scan Tools
    While many aftermarket scan tools can display most, if not all, of the parameters of the factory scan tool, there can be a difference when trying to troubleshoot some faults.

## Slide 24: Figure 85.11 Aftermarket Scan Tool
An enhanced aftermarket scan tool being used to diagnose an engine performance issue.

## Slide 25: Figure 85.12 Bluetooth Adapter
A Bluetooth adapter that plugs into the DLC and transmits global OBD-II information to a smart phone that has a scan tool app installed

## Slide 26: Animation: Scan Tools, OBD-II (Animation will automatically start)

## Slide 27: Animation: Scan Tools (Animation will automatically start)

## Slide 28: Animation: Automatic Scan Tools, History (Animation will automatically start)

## Slide 29: Animation: Scan Tools (IAC Test) (Animation will automatically start)

## Slide 30: Animation: Scan Tools, Automatic Transmission (Animation will automatically start)

## Slide 31: Question 2: ?
What is the difference between a factory level and an aftermarket scan tool?

## Slide 32: Answer 2
The factory scan tool supports a specific brand, whereas an aftermarket scan tool support many brands.

## Slide 33: Retrieval of Diagnostic Information
Locate and gain access to the data link connector (D L C).
Connect the scan tool to the D L C and establish communication.
Follow the on-screen instructions of the scan tool.
Observe the scan data, as well as any D T Cs.
Follow the vehicle manufacturer’s instructions if any D T Cs are stored.
Notes: NOTE See page 993 for Chart 85-2 Examples of observed scan tool data.

## Slide 34: Troubleshooting Using Diagnostic Trouble Codes
Pinning down causes of the actual problem can be accomplished by trying to set the opposite code.
  If the opposite code sets, this indicates that the wiring and connector for the sensor is okay and the sensor itself is defective (open).
  If the same code sets, this indicates that the wiring or electrical connection is open (has high resistance) and is the cause of the setting of the D T C.
Methods for Clearing Diagnostic Trouble Codes
  Scan tool, remove power from computer, or disconnect the vehicle battery.

## Slide 35: Retrieving Codes Prior to 1996
Flash Codes
  Most vehicles from the early 1980s through 1995 used some method to retrieve D T Cs.
  Scan Tool
  Special Tester
  Fused jumper wire
  Test light

## Slide 36: D L C locations
The data link connector (D L C) is a standardized 16-cavity connector to which a scan tool can be connected to retrieve diagnostic information from the vehicle’s computers
The normal location is under the dash on the driver’s side of the vehicle.

## Slide 37: Figure 85.13 DLC Location
The data link connector (DLC) can be located in various locations

## Slide 38: Figure 85.14 DLC
A typical OBD-II DLC. The location varies with make and model and may even be covered, but a tool is not needed to gain access. Check service information for the exact location, if needed

## Slide 39: Animation: Retrieving Trouble Codes, Code Reader (Animation will automatically start)

## Slide 40: Animation: Diagnostic Trouble Code, DTC (Animation will automatically start)

## Slide 41: O B D-I I Diagnosis
Starting with the 1996 model year, all vehicles sold in the United States must use the same type of 16-pin D L C and must monitor emissions-related components.
Retrieving O B D-I I Codes
  A scan tool is required to retrieve diagnostic trouble codes from most O B D-I I vehicles.
  Every O B D-I I scan tool will be able to read all generic Society of Automotive Engineers (S A E) D T Cs from any vehicle.

## Slide 42: Figure 85.15 Fiat-Chrysler DTCs
Diagnostic trouble codes (DTCs) from Chrysler and Dodge vehicles can be retrieved by turning the ignition switch to on and then off three times

## Slide 43: Manufacturer’s Diagnostic Routines (1 of 2)
O B D-I I Drive Cycles: vehicle must be driven under a variety of operating conditions for all active tests to be performed.
Types of O B D-I I Codes
  TYPE A CODES. A type A diagnostic trouble code is emissions related and causes the M I L to be turned on at the first trip if the computer has detected a problem.
  TYPE B CODES. A type B code is stored and the M I L is turned on during the second consecutive trip, alerting the driver to the fact that a diagnostic test was performed and failed.

## Slide 44: Manufacturers Diagnostic Routines (2 of 2)
  TYPE C AND D CODES. Type C and type D codes are for use with non-emissions-related diagnostic tests.
O B D-I I Freeze Frame
  O B D I I requires the computer to take a “snapshot” or freeze-frame of all data at the instant an emissions-related D T C is set.
Diagnosing Intermittent Malfunctions
  Determine the conditions when the malfunction occurs, and then try to duplicate those conditions.
Notes: TECH TIP: The Brake Pedal Trick
If the vehicle manufacturer recommends that battery power be disconnected, first disconnect the negative battery cable and then depress the brake pedal. Because the brake lights are connected to battery power, depressing the brake pedal causes all of the capacitors in the electrical system and computer(s) to discharge through the brake lights.
TECH TIP Drive the Light Out
If working on a vehicle that is subject to state emissions testing, it is best to not clear codes. When diagnostic trouble codes are cleared, all of the monitors have to be rerun and this can be a time-consuming job. Instead of clearing the code, simply drive the vehicle until
the PCM clears the code. This will likely take less time compared to trying to drive the vehicle under varying
conditions to run all of the monitors.

## Slide 45: Road Test (Drive Cycle)
The vehicle may have to be driven under conditions that allow the P C M to conduct monitor tests. This drive pattern is called a drive cycle.
The drive cycle is different for each vehicle manufacturer, but a universal drive cycle may work. In many cases, performing a universal drive cycle resets most monitors in most vehicles.
Notes: After the repair has been successfully completed, the vehicle should be driven under similar conditions that caused the original concern. Verify that the problem has been corrected. To per- form this test-drive, it is helpful to have a copy of the freeze-frame parameters that were present when the DTC was set. By driving under similar conditions, the PCM may perform a test of the system and automatically extinguish the MIL. This is the method preferred by most vehicle manufacturers. The DTC can be cleared using a scan tool, but then that means that monitors will have to be run and the vehicle may fail an emissions inspection if driven directly to the testing station.
PROCEDURES FOR RESETTING THE PCM The PCM can be reset or cleared of previously set DTCs and freeze-frame data in the following ways:
1. Driving the Vehicle. Drive the vehicle under similar con present when the fault occurred. If the conditions are similar and the PCM performed the noncontinuous monitor test and it passed three times, then the PCM will extinguish the MIL. This is the method preferred by most vehicle manufacturers; however, this method could be time consuming. If three passes cannot be achieved, the owner of the vehicle will have to be told that even though the check engine light (MIL) is on, the problem has been corrected and the MIL should go out in a few days of normal driving.
Clear DTCs Using a Scan Tool. A scan tool can be used to clear the diagnostic trouble code (DTC), which will also delete all of the freeze-frame data. The advantage of using a scan tool is that the check engine (MIL) will be out and the customer will be happy that the problem (MIL on) has been corrected. Do not use a scan tool to clear a DTC if the vehicle is going to be checked soon at a test station for state-mandated emissions tests.
Battery Disconnect. Disconnecting the negative battery cable will clear the DTCs and freeze-frame on many vehicles but not all. Besides clearing the DTCs, disconnecting the battery for about 20 minutes will also erase radio station presets and other memory items in many cases. Most vehicle manufacturers do not recommend that the battery be disconnected to clear DTCs and it may not work on some
vehicles.

## Slide 46: Engine Performance Videos and Animations
Videos Link: (A8) Engine Performance Videos
Animations Link: (A8) Engine Performance Animations

## Slide 47: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.