## Slide 1: Advanced Engine Performance Diagnosis
Eighth Edition
Chapter 7
In-Vehicle Engine Service
Copyright © 2025 Pearson Education, Inc. All Rights Reserved
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) Math Type Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)
INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
7.1 Explain thermostat replacement in engines.
7.2 Explain water pump replacement in engines.
7.3 Discuss intake manifold gasket inspection.
7.4 Discuss intake manifold gasket replacement.
7.5 Describe the steps involved in timing belt replacement.
7.6 Discuss hybrid engine precautions.
7.7 Discuss gasoline direct-injection engine concerns.

## Slide 3: Thermostat Replacement
Failure Patterns
  Stuck open
  Stuck closed
  Stuck partially open
  Skewed (does not operate in correct range)
Thermostat Replacement
  Allow system to cool, then drain.
  Replace thermostat per manufacturer’s instructions.
  Refill system and check for proper operation.

## Slide 4: Figure 7.1
Thermostat Jiggle Valve
If the thermostat has a jiggle valve, it should be placed toward the top to allow air to escape. If a thermostat were to become stuck open or open too soon, this can set a diagnostic trouble code P0128 (coolant temperature below thermostat regulating temperature).

## Slide 5: Animation: Thermostat Remove and Replace

## Slide 6: Question 1
What are the four pattern failures of a thermostat?

## Slide 7: Answer 1
Stuck open, stuck closed, stuck partially open, and skewed.

## Slide 8: Water Pump Replacement
Need for replacement:
  Coolant leaking from the weep hole.
  Bearing noisy or loose.
  Lack of proper coolant flow.
Replacement guidelines:
  Allow the system to cool, then drain.
  Remove and replace water pump per the manufacturer’s specifications.
  Refill system and verify proper operation.

## Slide 9: Figure 7.2
Removing Gasket
Use caution if using a steel scraper to remove a gasket from aluminum parts. It is best to use a wood or plastic scraper.

## Slide 10: Intake Manifold Gasket Inspection
To diagnose a possible leaking intake manifold gasket, perform the following tests.
  Visual inspection
  Coolant leak
  Air (vacuum) leak

## Slide 11: Figure 7.3
Failed Intake Gasket
An intake manifold gasket that failed and allowed coolant to be drawn into the cylinder(s).

## Slide 12: Intake Manifold Gasket Replacement
Allow the cooling system to cool, then drain.
Remove intake manifold making sure not to warp any components that will be reused.
Clean all surfaces.
Replace defective components per the manufacturer’s specifications.
Refill the cooling system and verify proper operation.

## Slide 13: Figure 7.4
Lower Intake Manifold
The lower intake manifold attaches to the cylinder heads.

## Slide 14: Figure 7.5
Upper Intake Manifold
The upper intake manifold, often called a plenum, attaches to the lower intake manifold.

## Slide 15: Figure 7.6
Pressure Relief Valve
Some plastic intake manifolds are equipped with a pressure relief valve that would open in the event of a backfire condition to prevent the higher internal pressures from causing damage to the manifold.

## Slide 16: Timing Belt Replacement
Timing belts are required to be replaced if any of the following occur:
  Manufacturer’s recommended timing belt replacement interval.
  Timing belt contaminated with coolant or engine oil.
  Timing belt has failed (missing belt teeth or broken).
Before replacing the timing belt make sure all needed special tools are available.

## Slide 17: Figure 7.7
Timing Belt
A single overhead camshaft engine with a timing belt that also rotates the water pump.

## Slide 18: Animation: Timing Belt, Remove and Replace

## Slide 19: Question 2
Why must timing belts be replaced?

## Slide 20: Answer 2
Replacement interval, fluid contamination, or physical damage.

## Slide 21: Engine Mount Replacement
Engine mounts are designed to perform the following functions:
  Support the weight and torque of the powertrain.
  Isolate noise and vibrations.
Inspection:
  Obvious damage or fluid leaks.
  Loose or damaged fasteners.
Replacement:
  Follow the manufacturer’s procedures when replacing.

## Slide 22: Animation: Remove and Replace Engine Mounts

## Slide 23: Figure 7.8
H E V Ready Light
A Toyota/Lexus hybrid electric vehicle has a ready light. If the ready light is on, the engine can start at anytime without warning.

## Slide 24: Hybrid Engine Precautions
Make sure the ignition is off and the key is out of the vehicle.
Check that the “Ready” light is off.
Do not touch any of the circuits with “orange” conduit.
Always use high-voltage lineman’s gloves when depowering the high-voltage system.

## Slide 25: Figure 7.9
S A E Viscosity
Always use the viscosity of oil as specified on the oil fill cap or published in service information or the owner’s manual.
Notes: Hybrid Engine Service
The gasoline engine in most hybrid electric vehicles specifies low-viscosity engine oil as a way to achieve maximum fuel economy. • See Figure 7.9. The viscosity required is often:
■ S A E 0W-16
■ S A E 0W-20
■ S A E 5W-20

## Slide 26: Question 3
Why is it important that the READY light be out on the dash before working under the hood of a hybrid electric vehicle?

## Slide 27: Answer 3
Any time the “Ready” light is illuminated, the vehicle may start.

## Slide 28: Figure 7.10
Carbon Issues
There may be a driveability issue because the gasoline direct-injection injector is exposed to combustion carbon and fuel residue.
Notes: Carbon Issues
Carbon deposits are often an issue in engines equipped with gasoline direct-injection systems. Carbon deposits are a result of poor fuel quality, or incorrect engine oil. The use of Top Tier Fuel, which contains a higher level of detergent, will help to reduce carbon deposits. Additionally, ensure the motor oil meets the original equipment manufacturers (O E M) requirement for the engine. Oils with an excessive level of vapor can lead to carbon deposits. Carbon deposits may be reduced with a pressurized induction tool. Stubborn carbon deposits will require the use of a media blaster. • See Figure 7.10. Check service information for the specified procedures to follow. Specified processes and procedures will likely restore power if the intake valves are coated.

## Slide 29: Valve Adjustment Step by Step

## Slide 30: Check Specifications
Notes: 1. Before starting the process of adjusting the valves, look up the specifications and exact procedures.

## Slide 31: Tools Necessary
Notes: 2. The tools necessary to adjust the valves on an engine with adjustable rocker arms include basic hand tools, feeler gauge, and a torque wrench.

## Slide 32: 4-Cylinder Engine Valves
Notes: 3. An overall view of the 4-cylinder engine that is due for a scheduled valve adjustment, according to the vehicle manufacturer’s recommendations.

## Slide 33: Disconnecting and Labeling Parts
Notes: 4. Start the valve adjustment procedure by first disconnecting and labeling, if necessary, all vacuum lines that need to be removed to gain access to the valve cover.

## Slide 34: Removing Air Intake Tube
Notes: 5. The air intake tube is being removed from the throttle body.

## Slide 35: Remove Valve Cover
Notes: 6. With all vacuum lines and the intake tube removed, the valve cover can be removed after removing all retaining bolts.

## Slide 36: Clean Engine
Notes: 7. Notice how clean the engine appears. This is a testament of proper maintenance and regular oil changes by the owner.

## Slide 37: Rotor Position Guide
Notes: 8. To help locate how far the engine is being rotated, the technician is removing the distributor cap to be able to observe the position of the rotor.

## Slide 38: Setting Timing Marks
Notes: 9. The engine is rotated until the timing marks on the front of the crankshaft line up with zero degrees—top dead center (T D C)—with both valves closed on #1 cylinder.

## Slide 39: Inserting Feeler Gauge
Notes: 10. With the rocker arms contacting the base circle of the cam, insert a feeler gauge of the specified thickness between the camshaft and the rocker arm. There should be a slight drag on the feeler gauge.

## Slide 40: Turn Valve Adjusting Screw
Notes: 11. If the valve clearance (lash) is not correct, loosen the retaining nut and turn the valve adjusting screw with a screwdriver to achieve the proper clearance.

## Slide 41: Rotate One Full Turn
Notes: 12. After adjusting the valves that are closed, rotate the engine one full rotation until the engine timing marks again align.

## Slide 42: Timing Marks Aligned Again
Notes: 13. The engine is rotated until the timing marks again align, indicating that the companion cylinder will now be in position for valve clearance measurement.

## Slide 43: Rotor Position Used Some Engines
Notes: 14. On some engines, it is necessary to watch the direction the rotor is pointing to help determine how far to rotate the engine.

## Slide 44: Larger & Smaller Feeler Gauges Used
Notes: 15. The technician is using a feeler gauge that is one thousandth of an inch thinner and another one thousandth of an inch thicker than the specified clearance as a double-check that the clearance is correct.

## Slide 45: Adjusting Valves Takes 2 Hands
Notes: 16. Adjusting a valve takes both hands—one to hold the wrench to loosen and tighten the lock nut and one to turn the adjusting screw.

## Slide 46: Replacing Gaskets and Seals
Notes: 17. After all valves have been properly measured and adjusted as necessary, start the reassembly process by replacing all gaskets and seals as specified by the vehicle manufacturer.

## Slide 47: Reinstall Valve Cover
Notes: 18. Reinstall the valve cover, being careful to not pinch a wire or vacuum hose between the cover and the cylinder head.

## Slide 48: Tighten to Specs
Notes: 19. Use a torque wrench and torque the valve cover retaining bolts to factory specifications.

## Slide 49: Reinstall Distributor Cap
Notes: 20. Reinstall the distributor cap.

## Slide 50: Reinstall Wires and Brackets
Notes: 21. Reinstall the spark plug wires and all brackets that were removed to gain access to the valve cover.

## Slide 51: Reconnect Vacuum Lines and Tubes
Notes: 22. Reconnect all vacuum and air hoses and tubes. Replace any vacuum hoses that are brittle or swollen with new ones.

## Slide 52: Reinstall Clips, Start Engine
Notes: 23. Be sure that the clips are properly installed. Start the engine and check for proper operation.

## Slide 53: Check for Leaks
Notes: 24. Double-check for any oil or vacuum leaks after starting the engine.

## Slide 54: Summary
Thermostats can fail in following ways:
  Stuck open/closed or stuck partially open, skewed
Water pump replaced if any of following are present:
  Leaking from the weep hole
  Noisy/Loose bearing
  Lack of normal circulation due to worn impeller blades
Leaking intake manifold gasket can cause coolant to get into the oil or oil into the coolant
When timing belt replaced, most O E M S recommend that following be replaced: Tensioner assembly, Water pump, seal(s)
When working on H E V be sure that the key is off and out of the ignition and the READY light is off.

## Slide 55: Animation and Video Library Links (Must have an internet connection and active Haldeman subscription)
Animation Library: (A8) Engine Performance Animations
Video Library: (A8) Engine Performance Videos

## Slide 56: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.