## Slide 1: Automotive Electrical and Engine Performance
Ninth Edition
Chapter 36
Gasoline Direct-Injection Systems
Copyright © 2025 Pearson Education, Inc. All Rights Reserved
Notes: If this PowerPoint presentation contains mathematical equations, you may need to check that your computer has the following installed:
1) Math Type Plugin
2) Math Player (free versions available)
3) NVDA Reader (free versions available)
INSTRUCTOR NOTE: This presentation includes text explanation notes, you can use to teach the course. When in SLIDE SHOW mode, you RIGHT CLICK and select SHOW PRESENTER VIEW, to use the notes.

## Slide 2: Learning Objectives
36.1 Explain how a direct fuel-injection system works.
36.2 Describe the direct-injection fuel delivery system.
36.3 Describe modes of operation.
36.4 Discuss G D I piston designs.
36.5 Discuss port/direct injection systems.
36.6 Discuss engine start systems.
36.7 Discuss G D I service issues.

## Slide 3: Direct Fuel Injection (1 of 2)
Port Injection v s. Direct Injection
  In G D I system, fuel is squirted directly into combustion chamber.
  In a port fuel-injection system, there is constant fuel pressure but variable injector pulse width.
  In a G D I, there is almost constant injector pulse width with varying fuel pressure.
Parts and Operation
  A direct-injection system sprays high-pressure fuel, up to 2,900 P S I, into the combustion chamber.

## Slide 4: Direct Fuel Injection (2 of 2)
Advantages of Gasoline Direct Injection
  Improved fuel economy and lower emissions
  Higher compression ratio for higher engine efficiency
  Use of lower-octane gasoline
  Higher volumetric efficiency
Disadvantages of Gasoline Direct Injection
  Higher cost due to high-pressure pump and injectors
  More components compared with port fuel injection
  Higher
  emissions

## Slide 5: Figure 36.1
P F I Compared to G D I
A comparison of a port fuel-injection system (right) to a gasoline direct-injection (G D I) system on the left.
Notes: Long Description:
In a direct injection system, fuel is sprayed directly into the combustion chamber by an injector. In a spray type fuel injection system, fuel is sprayed by a fuel injector upstream near the valve and air mixes with the fuel above the intake valve. The fuel injector is connected to a wiring connector and the fuel rail.

## Slide 6: Figure 36.2
G D I Injection
A gasoline direct-injection system injects fuel under high pressure directly into the combustion chamber.

## Slide 7: Question 1
What are two advantages of gasoline direct injection compared with port fuel injection?

## Slide 8: Answer 1
Better fuel economy and lower emissions.

## Slide 9: Direct-Injection Fuel Delivery System (1 of 2)
Low-Pressure Supply Pump
  The fuel pump in the fuel tank supplies fuel to the high-pressure fuel pump at a pressure of approximately 60 P S I.
High-Pressure Pump
  A typical G D I high-pressure pump has a range of between 500 P S I (3,440 k P a) and 2,900 P S I (15,200 k P a) during engine operation.

## Slide 10: Direct-Injection Fuel Delivery System (2 of 2)
Fuel Rail
  The fuel rail stores the fuel from the high-pressure pump and stores high-pressure fuel for use to each injector.
Fuel Pressure Regulator
  An electric pressure-control valve is installed between the pump inlet and outlet valves.

## Slide 11: Figure 36.3
Low-Pressure Pump
A G D I system uses a low-pressure pump in the gas tank similar to other types of fuel-injection systems. The P C M controls the pressure of the high-pressure pump using sensor inputs.
Notes: Long Description:
A fuel pump sucks fuel from the fuel tank and a low-pressure sensor is connected to the tank. The fuel pump is controlled by a fuel pump speed module, which has a transistor with the collector connected to 12 V. The base of the transistor is connected to the emitter of a transistor in the P C M circuit. The collector of this transitor is connected to B positive and the base to the second right pin of a 6-pin I C. The emitter is also connected to the sixth right pin of a 12-pin I C. The sixth left pin of the I C is connected to the low pressure sensor, while the fifth left pin is connected to the high pressure sensor. A high-pressure pump is connected to a fuel rail, which in turn has four G D I injectors connected to it. The P C M controls both the sensors and the speed module.

## Slide 12: Figure 36.4
G D I Uses 2 Fuel Pumps
A typical direct-injection system uses two pumps-one-low-pressure electric pump in the fuel tank and the other a high-pressure pump driven by the camshaft. The high-pressure fuel system operates at a pressure as low as 500 P S I during light load conditions and as high as 2,900 P S I under heavy loads.
Notes: Long Description:
A low-pressure fuel pump is installed inside a fuel tank and is connected to a pressure regulator. The pressure regulator houses a high-pressure fuel pump and is connected to a common rail. A high-pressure pump drive lobe is located on the engine camshaft and drives the high-pressure pump. An injector is connected to the common rail.

## Slide 13: Figure 36.5
High-Pressure Pump
(a) A typical camshaft-driven high-pressure pump used to increase fuel pressure to 2,000 P S I or higher. (b) The high-pressure pump assembly removed from the engine. Many G D I engines use a roller where the high-pressure pump rides against the cam lobes to help reduce friction and wear.

## Slide 14: Figure 36.6
G D I Fuel Rail
A G D I fuel rail and pump assembly with the electric pressure-control valve.

## Slide 15: Animation: Direct Fuel Injection

## Slide 16: Chart 36.1
P F I v s G D I
A comparison chart showing the major differences between a port fuel-injection system and a G D I system.
Notes: Long Description:
The table is titled port fuel-injection system compared with G D I system. The table has two columns: port fuel injection and gasoline direct injection. Row entries are as follows. Fuel pressure. Port fuel injection: 35 to 60 pounds per square inch. Gasoline direct injection: Lift pump, 50 to 60 pounds per square inch. High-pressure pump, 500 to 2,900 pounds per square inch. Injection pulse width at idle. Port fuel injection: 1.5 to 3.5 milliseconds. Gasoline direct injection: About 0.4 milliseconds, 400 microseconds. Injector resistance. Port fuel injection: 12 to 16 ohms. Gasoline direct injection: 1 to 3 ohms. Injector voltage. Port fuel injection: 6 volts for low-resistance injectors, 12 volts for most injectors. Gasoline direct injection: 50 to 90 volts. Number of injections per event. Port fuel injection: one. Gasoline direct injection: 1 to 3. Engine compression ratio. Port fuel injection: ratio of 8 to 1 to ratio of 11 to 1. Gasoline direct injection: ratio of 11 to 1 to ratio of 13 to 1.

## Slide 17: Gasoline Direct-Injection Fuel Injectors
Each high-pressure fuel injector assembly is an electrically magnetic injector mounted in the cylinder head.
The P C M controls each fuel injector with 50 to 90 volts (usually 60 to 70 volts), depending on the system, which is created by a boost capacitor in the P C M.

## Slide 18: Modes of Operation (1 of 2)
Stratified Mode
  In this mode of operation, the air–fuel mixture is richer around the spark plug than it is in the rest of the cylinder.
Homogeneous Mode
  In this mode of operation, the air–fuel mixture is the same throughout the cylinder.

## Slide 19: Modes of Operation (2 of 2)
There are variations of these modes that can be used to fine-tune the air–fuel mixture inside the cylinder.
  Homogeneous lean mode
  Homogeneous stratified mode
  Homogeneous knock protection mode
  Stratified catalyst heating mode

## Slide 20: Piston Top Designs
Three of the most commonly used designs include:
  Spray-guided combustion
  Swirl combustion
  Tumble combustion

## Slide 21: Figure 36.7
Injector at Top
In this design, the fuel injector is at the top of the cylinder and sprays fuel into the cavity of the piston.

## Slide 22: Figure 36.8
Swirl Combustion
The side injector combines with the shape of the piston to create a swirl as the piston moves up on the compression stroke.

## Slide 23: Figure 36.9
Tumbling Force
The piston creates a tumbling force as it moves upward.

## Slide 24: Question 2
What are the two primary modes of operation?

## Slide 25: Answer 2
Stratified and homogeneous mode.

## Slide 26: Port- and Direct-Injection Systems
Overview
  This system combines direct-injection injectors located in the combustion chamber with port fuel-injectors in the intake manifold near the intake valve.
Cold-Start Warm-Up
  To help reduce exhaust emissions after a cold start, the fuel system uses a stratified change mode.
  The catalytic converter rapidly reaches operating temperature, which reduces exhaust emissions.

## Slide 27: Figure 36.10
Notice that there are conditions when the port fuel injector, located in the intake manifold, and the gasoline direct injector, located in the cylinder, both operate to provide the proper air–fuel mixture.

## Slide 28: Gasoline Direct-Injection Issues
Noise Issues
  Injectors can often be heard with the engine running and the hood open. (Likely a normal condition)
Carbon Issues
  Carbon can accumulate on the tip of the injector.
  Carbon can accumulate on the back side of the intake valve.

## Slide 29: Figure 36.11
Drivability Issue
There may become a driveability issue because the G D I injector is exposed to combustion carbon and fuel residue.

## Slide 30: G D I Service
Carbon Prevention
  Dispersant every six months or every 6,000 miles has proven to help prevent injector and intake valve deposits.
Service Precautions
  Don’t reuse high-pressure lines.
  Always use a torque wrench when tightening fuel line fittings.
  Do not loosen any fuel fittings with the engine cranking or running.
  Always replace the Teflon seal whenever replacing or reinstalling a G D I injector.

## Slide 31: Figure 36.12
Carbon Prevention
Carbon Cleaning: More sophisticated cleaning methods include pressurized induction tools that provide a mist of dispersant through the air intake system and media blasters that use a pressurized abrasive to remove carbon.
Notes: Carbon Prevention
Most experts recommend the use of Techronő a fuel system dispersant, to help keep carbon from accumulating. The use of a dispersant every six months or every 6,000 miles has proven to help prevent injector and intake valve deposits. The use of Top Tier fuel is also recommended to help reduce the deposits on intake valves and injectors. Top Tier fuel contains a higher level of detergent than standard fuels. Visit https://www.toptiergas.com to identify what brands sell Top Tier fuel and where stations that sell the fuel are located.
If the lack of power is discovered and there are no stored diagnostic trouble codes, a conventional carbon cleaning procedure will likely restore power if the intake valves are coated. Cleaning tools can be as simple as a wire brush and solvent. More sophisticated
cleaning methods include pressurized induction tools that provide a mist of dispersant through the air intake system and media blasters that use a pressurized abrasive to remove the carbon. • See Figure 36.12.

## Slide 32: Figure 36.13
Ball and Socket
The high-pressure lines use a ball and socket connection. The ball end deforms when the line is tightened and must be replaced with a new part whenever it is removed.

## Slide 33: Figure 36.14
G D I Injector
Whenever a G D I fuel injector is removed, a new Teflon seal must be installed to ensure a leak-free connection in the combustion chamber.

## Slide 34: Question 3
What should be replaced any time a high-pressure injector is serviced?

## Slide 35: Answer 3
The Teflon seal.

## Slide 36: Summary
G D I system uses a fuel injector that delivers a short squirt of fuel directly into the combustion chamber rather than in the intake manifold, near the intake valve on a port fuel-injection system.
Advantages of using gasoline direct injection:
  Improved fuel economy
  Reduced exhaust emissions
  Greater engine power
Some of the disadvantages of G D I:
  Higher cost
  The need for N O x storage catalyst in some applications
  More components
The operating pressure can vary from as low as 500 P S I during some low-demand conditions to as high as 2,900 P S I.

## Slide 37: Animations and Video Links (Halderman website subscription and web access needed to view)
(A8) Engine Performance Animations
(A8) Engine Performance Videos

## Slide 38: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.